## Slide 1
CERN strategy
& future large scale projects
F. Zimmermann, CERN/BE
Work supported by the European Commission under Capacities 7th Framework Programme, Grant Agreement 312453
gratefully acknowledging input from FCC global design study & CepC team
special thanks to M. Benedikt, D. Schulte, S. Stapnes, J. Wenninger
Channeling2014 Conference, Capri, 5 October 2014

## Slide 2
LEP – highest energy e+e- collider so far
maximum c.m. energy 209 GeV
maximum synchrotron radiation power 23 MW

## Slide 3
Large Hadron Collider (LHC)
design:
c.m. energy 14 TeV (pp);
luminosity 1034 cm-2s-1; 1.15x1011 p/bunch;
2808 bunches/beam;
360 MJ / beam
1983 first LHC proposal, launch of design study
1994 CERN Council: LHC approval
2010 first collisions at 3.5 TeV beam energy
2015 collisions at design energy (plan)
now is the time to plan for 2040!

## Slide 4
With the discovery of a Higgs boson in 2012, we have completed the Standard Model (almost 80 years of theoretical and experimental efforts !)
However: SM is not a complete theory
Several outstanding questions (e.g. composition of dark matter, cause of universe’s accelerated expansion [dark energy / inflation], origin of matter-antimatter asymmetry, neutrino masses, why 3 families?, lightness of Higgs boson, weakness of gravity, … ) which cannot be explained within the SM.
These questions require NEW PHYSICS
Prospects for Particle Physics
Present knowledge is insufficient to determine energy scale of new physics ; LHC will provide new information from pp collisions at higher cm energy (13 TeV) by 2017-18
F. Gianotti et al.

## Slide 5
main questions in particle physics and main approaches to address them
question | high-energy colliders | high-precision experiments | neutrino experiments | dedicated searches | cosmic surveys
Higgs, EWSB | X |  |  |  | 
neutrinos | X |  | X | X | X
dark matter | X |  |  | X | 
flavour, CP violation | X | X | X | X | 
new particles and forces | X | X | X | X | 
universe acceleration |  |  |  |  | X
most of these questions require high-energy and/or
high-intensity accelerators
F. Gianotti et al.

## Slide 6
Run 2
Run 3
Run 4
LS 2
LS 3
LS 4
LS 5
Run 5
LS2 starting in 2018 (July) => 18 months + 3 months BC
LS3 LHC: starting in 2023 => 30 months + 3 months BC
Injectors: in 2024 => 13 months + 3 months BC
LHC roadmap: schedule until 2035
Beam commissioning
Technical stop
Shutdown
Physics
Run 2
Run 3
Run 4
LS 2
LS 3
LS 4
LS 5
Run 5
(Extended) Year End Technical Stop: (E)YETS
EYETS
YETS
YETS
YETS
YETS
YETS
300 fb-1
3’000 fb-1
30 fb-1
PHASE 1
PHASE 2
F. Bordry
Phase 2: HL-LHC

## Slide 7
3000 fb-1 delivered in the order of 10 years
High “virtual” luminosity with levelling anticipated
Challenging demands on the injector complex
  major upgrades foreseen
5 x 1034 cm-2s-1
levelled luminosity
Pile-up ~140
3 fb-1 per day
~250 fb-1 /year
M. Lamont
HL-LHC

## Slide 8
technology transition: Nb-Ti →Nb3Sn
O. Bruning

## Slide 9
more than 1.2 km of LHC plus technical infrastructure
(e.g. Cryo and Powering)
Nb3Sn dipoles & quadrupoles
ATLAS
New quadrupole triplet based on Nb3Sn (12 T at coil)
required due to:
-Radiation damage
-Need for more aperture
Changing the triplet region is not enough for reaching the HL-LHC goal!
2. We also need to modify a large part of the matching section
e.g. Crab Cavities &
D1, D2, Q4 & corrector
3. For collimation we also need to change the DS in the continuous cryostat: 11-T Nb3Sn dipole
CMS
O. Brüning,
L. Rossi
HL-LHC - critical zones around IP1 & IP5

## Slide 10
MBHSP02 (1 m) passed 11 T field during training at 1.9 K with I = 12080 A on 5 March 2013
FNAL: Nb3Sn dipole demonstrators
US-LARP

## Slide 11
International Linear Collider (ILC)
total length ~30 (500 GeV) - 50 km (1 TeV)
SC acceleration structures ~ 30 MV/m; TDR completed in 2012, ILC technology used for XFEL at DESY; present optimistic time line: construction start in 2018 & 1st physics in 2027?

## Slide 12
International Linear Collider (ILC) - 2
Japanese HEP community expressed interest in hosting the ILC. Site chosen: 北上市 (Kitakami) in Northern Japan. Under review by Japanese ministry MEXT.
Courtesy F. Simon

## Slide 13
European Strategy Update 2013
“CERN should undertake design studies for accelerator projects in a global context, with emphasis on proton-proton and electron-positron high-energy frontier machines.”
strategy adopted by the CERN Council
http://cds.cern.ch/record/1567258/files/esc-e-106.pdf

## Slide 14
total length (main linac) ~11 (500 GeV) - 48 km (3 TeV)
Compact Linear Collider (CLIC)
accelerating gradient
~100 MV/m
key technologies: 2-beam accel., drive-beam , X-band RF

## Slide 15
CLIC Conceptual Design Report 2012
~1400 authors, ~1200 pages
Vol 1: The CLIC accelerator and site facilities (H.Schmickler)
- CLIC concept with exploration over multi-TeV energy range up to 3 TeV
- Feasibility study of CLIC parameters optimized at 3 TeV (most demanding)
- Consider also 500 GeV, and intermediate energy range
- Complete, presented in SPC in March 2011, in print: https://edms.cern.ch/document/1234244/
Vol 2: Physics and detectors at CLIC (L.Linssen)
- Physics at a multi-TeV CLIC machine can be measured with high precision, despite challenging background conditions
- External review procedure in October 2011
- Completed and printed, presented in SPC in December 2011 http://arxiv.org/pdf/1202.5940v1
Vol 3: “CLIC study summary” (S.Stapnes)
- Summary and available for the European Strategy process, including possible implementation stages for a CLIC machine as well as costing and cost-drives
- Proposing objectives and work plan of post CDR phase (2012-16)
- Completed and printed, submitted for the European Strategy Open Meeting
in September http://arxiv.org/pdf/1209.2543v1
In addition a shorter overview document was submitted as input to the European Strategy update, available at:
http://arxiv.org/pdf/1208.1402v1

## Slide 16
Future Circular Collider Study - SCOPE
CDR and cost review for the next ESU (2018)
Forming an international collaboration to study:
pp-collider (FCC-hh)  defining infrastructure requirements
80-100 km infrastructure in Geneva area
e+e- collider (FCC-ee) as potential intermediate step
p-e (FCC-he) option
~16 T  100 TeV pp in 100 km
~20 T  100 TeV pp in 80 km

## Slide 17
Qinhuangdao (秦皇岛）
50 km
70 km
easy access
300 km from Beijing
3 h by car
1 h by train
Yifang Wang
CepC, SppC
CepC/SppC study (CAS-IHEP), CepC CDR end of 2014, e+e- collisions ~2028; pp collisions ~2042
“Chinese Toscana”

## Slide 18
CepC/SppC project – recent news in Nature
24 J U LY 2014 | VO L 511 | NAT U R E | 3

## Slide 19
previous studies in Italy (ELOISATRON 300 km), US (SSC 87 km, VLHC/VLLC 233 km) & Japan (94 km)
ex. SSC
Supercolliders Superdetectors: Proceedings of the 19th and 25th Workshops of the INFN Eloisatron Project
ex. ELOISATRON
SSC CDR 1986
H. Ulrich Wienands, The SSC Low Energy Booster: Design and Component Prototypes for the First Injector Synchrotron,
IEEE Press 1997
VLHC Design Study Group Collaboration June 2001. 271 pp.
SLAC-R-591, SLAC-R-0591, SLAC-591, SLAC-0591, FERMILAB-TM-2149
http://www.vlhc.org/
ex. VLHC
ex. TRISTAN-II
study 1983

## Slide 20
Courtesy V. Shiltsev
pp
e+e-
factor 10 every
20-30 years
factor 10 every
10 years
factor 105-107 in e+e-
luminosity
collider c.m. energy vs. year
Ecm=2ec Br
hadron-lepton
FCC-he
LHeC
ep

## Slide 21
FCC-hh: 100 TeV pp collider
LHC
27 km, 8.33 T
14 TeV (c.m.)
FCC-hh (alternative)
80 km, 20 T
100 TeV (c.m.)
FCC-hh (baseline)
100 km, 16 T
100 TeV (c.m.)
“HE-LHC”
27 km, 20 T
33 TeV (c.m.)
Geneva
PS
SPS
LHC
L. Bottura
B. Strauss

## Slide 22
➥ Access to new particles in the few TeV to 30 TeV mass range, beyond LHC reach
➥ Immense/much-increased rates for
phenomena in the sub-TeV mass range →
increased precision w.r.t. LHC and possibly ILC
➥ Access to very rare processes in the sub-TeV mass range → search for stealth phenomena, invisible at the LHC
FCC-hh opens three physics windows
M. Mangano

## Slide 23
FCC-hh Key Parameters
Parameter | FCC-hh | LHC
Energy | 100 TeV c.m. | 14 TeV c.m.
Dipole field | 16 T | 8.33 T
# IP | 2 main, +2 | 4
Luminosity/IPmain | 5 x 1034 cm-2s-1 | 1 x 1034 cm-2s-1
Energy/beam | 8.4 GJ | 0.39 GJ
Synchr. rad. | 28.4 W/m/apert. | 0.17 W/m/apert.
Bunch spacing | 25 ns (5 ns) | 25 ns
Preliminary, subject to evolution

## Slide 24: ring optics for alternative layouts
R. Alemany,
B. Holzer,
R. Tomas,
D. Schulte
bx,y [m]
Dx [m]
LHC-like
circular
SSC-like
race-
track
C=99.13 km
C=100.8 km
Linsertion~7.4 km
work in progress
FODO arc
optics,
cell length
~200 m

## Slide 25
only a quarter is shown
15-16 T: Nb-Ti & Nb3Sn
20 T: Nb-Ti & Nb3Sn & HTS
L. Rossi, E. Todesco, P. McIntyre
“hybrid magnets”
example block-coil layout
cost-optimized high-field dipole magnets

## Slide 26: From ITER- to HEP-class Nb3Sn
ITER
US-CDP
CARE-NED
EuCARD
HL-LHC
HL-LHC specs
FCC
FCC specs
L. Bottura

## Slide 27: machine protection
energy per proton beam
LHC: 0.4 GJ → FCC-hh: 8 GJ (20x more !)
  kinetic energy of Airbus A380 at 720 km/h
  can melt 12 tons of copper, or drill a 300-m long hole

## Slide 28: Crystal Collimation
LHC-type solution is baseline, but other approaches should be investigated:
hollow e- beam as collimator
crystals to extract particles
renewable collimators
D. Schulte,
S. Redaelli
A. Lobko,
V. Tikhomirov,
INP Minsk
Volume reflection mode
− multiple volume reflection effect
− increases deflection angle to 5 times

## Slide 29: crystal extraction experiment UA9

Channeling peak
Reflection range
Amorphous orientation
Amorphous orientation
× 5 reduction rate
Angle [mrad]
-1700
-1800
-1600
counts
100
500
-1500
Nuclear loss rate seen by a scintillator telescope downstream of the crystal
Nuclear loss rate (including diffractive) strongly depressed
W. Scandale
SPS
2009

## Slide 30: staging of crystal deflectors
schematic layout
of the experimental setup used to
study multiple volume reflection at the H8 beam line of the CERN SPS
W. Scandale et al, Observation of Multiple Volume Reflection of Ultrarelativistic Protons by a Sequence of Several Bent Silicon Crystals, Phys.Rev.Lett. 102 (2009) 084801
6 strip crystals in series
(each 2 mm long):
400 GeV/c protons
reflected by 40±2 mrad
[effective field 16 T]
with efficiency 0.93±0.04
quasimosaic
strip
crystals
proof of principle demonstration!

## Slide 31: Crystal Calorimetry
strong-field QED effects enhance radiation and pair production:
production and measurement of e-, g & hyperon polarization;
reduced radiation length and calorimeter thickness;
increased mass resolution
A. Lobko,
INP Minsk

## Slide 32: FCC-hh injector complex
B. Goddard,
W. Herr, et al.
based on existing & planned (HL-LHC/LIU) injector chain;
HEB in LHC tunnel (e.g. modified LHC) or FCC tunnel
crystal extraction for
fixed target physics?!
W. Scandale

## Slide 33: physics requirements for FCC-ee
highest possible luminosity for a wide physics program ranging from the Z pole to the production threshold
  beam energy range from 45 GeV to 175 GeV
main physics programs / energies:
  Z (45.5 GeV): Z pole, ‘TeraZ’ and high precision MZ & GZ,
  W (80 GeV): W pair production threshold,
  H (120 GeV): ZH production (maximum rate of H’s),
  t (175 GeV): threshold
some polarization up to ≥80 GeV for beam energy calibration
optimized for operation at 120 GeV?!

## Slide 34
FCC-ee Key Parameters
Parameter | FCC-ee | LEP2
Energy/beam | 45 – 175 GeV | 105 GeV
Bunches/beam | 98 – 16700 | 4
Beam current | 6.6 – 1450 mA | 3 mA
Luminosity/IP | 1.8-28 x 1034 cm-2s-1 | 0.0012 x 1034 cm-2s-1
Energy loss/turn | 0.03-7.55 GeV | 3.34 GeV
Synchr. power | 100 MW | 22 MW
RF Voltage | 2.5 – 11 GV | 3.5 GV
Preliminary, subject to evolution

## Slide 35: layout & optics at 120 & 175 GeV
S
B
Q
B = bending magnet, Q = quadrupole, S = sextupole
Q
B
BPM
Corrector
B
B
S
Q
arc cell
Lattice V12b-s
Circumference: 100 km
Arc length: 2 × 3.4 km
Straight section: 1.5 km
layout
B. Harer, B. Holzer
0
20
40
60
80
100
0
2
4
6
8
10
12
b
e
t
x
i
n
m
s in km
FODO cell optics
cell length 50 m
full ring optics

## Slide 36: optics 175 & 120 → 80 & 45.5 GeV
example: 100 m cell length
example: 300 m cell length
80 GeV
45.5 GeV
B. Harer, B. Holzer
all emittances ex ≤ 0.5 baseline

## Slide 37: SC RF System
RF system requirements are characterized by two regimes.
  High gradients for H and – up to ~11 GV.
  High beam loading with currents of ~1.5 A at the Z pole.
RF system must be distributed over the ring to minimize energy excursions (~4.5% energy loss @ 175 GeV).
  Optics errors driven by energy offsets, effect on h.
Aiming for SC RF cavities with gradients of ~20 MV/m.
RF frequency of 400 or 800 MHz (current baseline).
  Nano-beam / crab waist favors lower frequency, e.g. 400 MHz.
Conversion efficiency (wall plug to RF power) is critical. Aiming for 75% or higher  R&D !
  An important item for FCC-ee power budget.~65% achieved for LEP2.
J. Wenninger, A. Butterworth, E. Jensen, et al.

## Slide 38: luminosity
H  1
Hour-glass
2F
F  1
Crossing angle
Beam-beam parameter
J. Wenninger

## Slide 39: beam-beam parameter
beam-beam parameter x measures strength of field sensed by the particles in a collision
beam-beam parameter limits are empirically scaled from LEP data (also 4 IPs)
In reasonable agreement with first simulations for FCC ee
The beam-beam limit may be raised significantly with Crab-Waist schemes !
J. Wenninger, R. Assmann, S. White, K. Ohmi, D. Shatilov, et al.
R. Assmann & K. Cornelis, EPAC2000

## Slide 40: beamstrahlung
hard photon emission at the IPs, ‘Beamstrahlung’, can become lifetime / performance limit for large bunch populations (N), small hor. beam size (sx) & short bunches (ss)
r : mean bending radius at the IP (in the field of the opposing bunch)
to ensure an acceptable lifetime, rh must be sufficiently large
  flat beams (large sx) !
  bunch length !
  large momentum acceptance of the lattice: 1.5 – 2% required.
    LEP: < 1% acceptance, SuperKEKB ~ 1-1.5%.
h : ring energy acceptance
g
e
e
lifetime expression by V. Telnov, modified version by A. Bogomyagkov et al
J. Wenninger, et al

## Slide 41: beam-beam limits: 2 regimes
Chart: beam energy (GeV)
| 100 | 110 | 120 | 130 | 140 | 150 | 160 | 175 | 180 | 190 | 200
beam-beam limit | 0.072102 | 0.080838 | 0.089735 | 0.098782 | 0.10797 | 0.11729 | 0.12673 | 0.14112 | 0.14597 | 0.15576 | 0.16565
vertical emittance 2pm, momentum acceptance 2% | 0.22589 | 0.22589 | 0.14393 | 0.14393 | 0.11174 | 0.11174 | 0.10395 | 0.10395 | 0.083959
vertical emittance 2pm, momentum acceptance 1.5% | 0.1969 | 0.1969 | 0.11894 | 0.11894 | 0.085458 | 0.085458 | 0.071965 | 0.071965 | 0.068366 | 0.068366 | 0.058671
beamstrahlung
lifetime w. h=1.5%
beamstrahlung
lifetime (300 s) w. h=2.0%
ey = 2 pm,
by* = 1 mm
M. Koratzinos, A. Bogomyagkov, E. Levichev, D. Shatilov, K. Yokoya, V. Telnov, K. Oide, …

## Slide 42
e+e- luminosity vs energy
additional ILC upgrades
(Harrison, Ross, Walker, 2013)
FCC-ee crab waist / improved optics
(Bogomyagkov, Levichev, Piminov, Shatilov, 2014)

## Slide 43: FCC-ee injection
beside the collider ring(s), a booster of the same size (same tunnel) must provide beams for top-up injection
  same size of RF system, but low power (~ MW)
  top up frequency ~0.1 Hz
  booster injection energy ~20 GeV
  bypass around the experiments
injector complex for e+ and e- beams of 10-20 GeV
  Super-KEKB injector ~ almost suitable
A. Blondel

## Slide 44: SuperKEKB = FCC-ee demonstrator
beam commissioning will start in 2015
top up injection at high current
by* =300 mm (FCC-ee: 1 mm)
lifetime 5 min (FCC-ee: ≥20 min)
ey/ex =0.25% (similar to FCC-ee)
off momentum acceptance (±1.5%, similar to FCC-ee)
e+ production rate (2.5x1012/s, FCC-ee: <1.5x1012/s (Z cr.waist)
SuperKEKB goes beyond FCC-ee, testing all concepts
K. Oide et al.

## Slide 45
Precision Measurements
Springboard for sensitivity to new physics
Theoretical issues:
  Higher-order QCD
  Higher-order EW
  Mixed QCD + EW
Rare Decays
Direct searches for new physics
Many opportunities
Z: 1012
b, c, τ: 1011
W: 108
H: 106
t: 106
The Twin Frontiers of FCC-ee Physics
J. Ellis
P. Janot
M. Ruan
M. Bicer et al., “First Look at the Physics Case of TLEP,’’ JHEP 01, 164 (2014)
S. Dawson et al., arXiv:1310.8361v2
Higgs coupling
measurements
HL-LHC
ILC500
FCC-ee 350
CepC, 4/ab

## Slide 46
faster electromagnetic shower generation
smaller electromagnetic calorimeters
generation or measurement of beam polarization
enhanced positron sources
e± crystal collimation
…
Crystal applications for FCC-ee, ILC or CLIC

## Slide 47
FCC-he: high-energy lepton-hadron collider
RR LHeC:
new ring
in LHC tunnel,
with bypasses
around
experiments
LR LHeC:
recirculating
linac with
energy
recovery
similar two options for FCC:
(1) FCC-ee ring, (2) ERL – from LHeC or new
LHeC CDR , published in 2012

## Slide 48
FCC Key Technologies
16 T superconducting magnets
Superconducting RF cavities
RF power sources
Affordable & reliable cryogenics
Reliability & availability concepts

## Slide 49
Future Circular
Collider Study
Large scale technical infrastructures
Conceptual design study 2014 – 2018
Driven by international contributions
Establish long-term liaisons with industry
Collaborate on technology evolution (> 2025)
Notes: CERN

## Slide 50
presently signing FCC MoUs with partners

## Slide 51
FCC MoU’s 3 Oct. 2014
ALBA/CELLS, Spain
BINP, Russia
CASE (SUNY/BNL), USA
CBPF, Brazil
CERN, Switzerland (Int’l)
CIEMAT, Spain
CNRS, France
Cockcroft Institute, UK
CSIC/IFIC, Spain
DESY, Germany
EPFL, Switzerland
Gangneung-Wonju Nat. U., Korea
Goethe U. Frankfurt, Germany
GSI, Germany
Hellenic Open U, Greece
IFJ PAN Krakow, Poland
INFN, Italy
INP Minsk, Belorussia
IPM, Iran
JAI/Oxford, UK
KEK, Japan
King’s College London, UK
MEPhI, Russia
Northern Illinois U., USA
NC PHEP Minsk, Belorussia
Sapienza/Roma, Italy
UC Santa Barbara, USA
TU Darmstadt, Germany
TU Tampere, Finland
U. Geneva, Switzerland
U. Iowa, USA
U Silesia, Poland

## Slide 52
Study Coordination
Hadron Collider Physics and Experiments
Lepton Collider Physics and Experiments
Hadron Injectors
Hadron Collider
Lepton Collider
e-p Physics, Experiments, IP Integration
Infrastructures and Operation
Lepton Injectors
Accelerator R & D Technologies
F. Gianotti, A. Ball, M. Mangano
A. Blondel, J. Ellis, P. Janot
M. Klein, O. Bruning
B. Goddard
D. Schulte, M. Syphers, J.M. Jimenez
Y. Papaphilippou (tbc)
J. Wenninger, U. Wienands, J.M. Jimenez
M. Benedikt, F. Zimmermann
P. Lebrun, P. Collier
F. Sonnemann, P. Lebrun
FCC Study Coordination Group
Costing Planning
M. Benedikt, F. Zimmermann

## Slide 53
FCC Collaboration Board
preparatory meeting 9-10 September 2014 at CERN (~80 participants, 1 / inst.)
Leonid “Lenny” Rivkin (EPFL & PSI) unanimously elected as interim Collaboration Board Chair

## Slide 54
FCC Horizon 2020 Design Study Proposal
submitted to Brussels on
2 September 2014
key aspects of 100 TeV energy frontier hadron collider:
conceptual design, feasibility, implementation scenario

## Slide 55
Physics and Experiments
Accelerators
Infrastructures and Operation
Implementation and Planning
Study and Quality Management
Hadron Collider Physics
Hadron Collider Experiments
Lepton Collider Physics
Lepton Collider Experiments
Lepton-Hadron Collider Physics
Lepton-Hadron Collider Experiment
Hadron Injectors
Hadron Collider
Lepton Injectors
Lepton Collider
Lepton-Hadron Collider
Technology R&D
Civil Engineering
Technical Infrastructures
Operation and Energy Efficiency
Integration
Computing and Data Services
Safety, RP and Environment
Project Risk Assessment
Implementation Scenarios
Cost Models
Study Administration
Communications
Conceptual Design Report
Work Breakdown Structure

## Slide 56
Physics and Experiments
Accelerators
Infrastructures and Operation
Implementation and Planning
Study and Quality Management
Hadron Collider Physics
Hadron Collider Experiments
Lepton Collider Physics
Lepton Collider Experiments
Lepton-Hadron Collider Physics
Lepton-Hadron Collider Experiment
Hadron Injectors
Hadron Collider
Lepton Injectors
Lepton Collider
Lepton-Hadron Collider
Technology R&D
Civil Engineering
Technical Infrastructures
Operation and Energy Efficiency
Integration
Computing and Data Services
Safety, RP and Environment
Project Risk Assessment
Implementation Scenarios
Cost Models
Study Administration
Communications
Conceptual Design Report
WBS – H2020 EU DS proposal

## Slide 57
HEP Timescale
1980
1985
1995
2000
2005
2010
2015
2020
2025
2030
2035
1990
Physics
25 years
Today
CDR & Cost
Construction
Physics
Upgr
LEP
Construction
Physics
Proto
Design
LHC
Construct
Physics
Design
HL-LHC
Construction
Proto
Design
Future Collider

## Slide 58
First FCC Week
Conference
Washington DC
23-27 March 2015
http://cern.ch/fccw2015

## Slide 59: how to go further?

## Slide 60: circular crystal collider?
cryogenic?
crystal
bending
stage
cryogenic?
crystal
bending
stage
proton beam
tunnel mostly empty
energy ramp using induction acceleration?
a dream or our future ?

## Slide 61
PSB
PS (0.6 km)
SPS (6.9 km)
HL-LHC
FCC-ee (80-100 km,
e+e-, up to 350
or 500 GeV c.m.)
FCC-hh
(pp up to
100 TeV c.m.
& AA)
FCC-he: e± (60-250 GeV) – p(50 TeV)/A collisions
≥50 years e+e-, pp, e±p/A physics at highest energies
LHeC & SAPPHiRE (gg)
LHC (26.7 km)
LHeC as FCC-ee injector?
LHeC-based FCC-he collider?!
FCC-he as ring-ring
collider ?!
possible evolution of FCC complex
followed by >1 PeV circular crystal collider (CCC)?!?
CCC,
> 1 PeV

## Slide 62: and on the linear route …

## Slide 63: dielectric & plasma accelerators
dielectric materials (quartz, diamond, garnets,.)
higher breakdown limits than metals;
dielectric structures driven in THz,
optical or near-IR regime
G=1-3 GV/m
driven by e- beam or by laser (external fiber laser or
integrated semiconductor laser)
plasma acceleration
G≈ 100 GV/m (n0 [1018 cm-3])1/2 ; n0≈1017-1018 cm-3
driven by laser, e- beam, or p beam
Kostyukov, Nerush, Litvak, 2012
unlimited acceleration is predicted to be possible ?!

## Slide 64
acceleration in crystal channels
G≈ 10 TV/m (n0 [1022 cm-3])1/2 ; n0 ≈1022-1023 cm-3
driven by x-ray laser
max. energy set by radiation emission due to betatron oscillations between crystal planes
Emax ≈300 GeV for e+, 104 TeV m, 106 TeV for p ?! Chen & Noble 1997; Dodin & Fisch 2008; Shiltsev ‘12
[is there no equivalent limit for lower-density plasmas?]
10 TV/m – disposable crystal accelerator
or 0.1 TV/m – reusable crystal accelerator
side injection of x-ray pulses using long fibers
now/soon available!
LCLS, Spring-8, XFEL, SwissFEL …
crystal accelerators

## Slide 65
linear X-ray crystal m collider
Vladimir Shiltsev, 2012
e± may soon run out of steam in the
high-gradient world!
→ need to change particle type
issues:
m production rate
neutrino radiation
earth
m linac 1
m linac 2
n beam
n beam

## Slide 66: highest-energy particles
4 July 2012 CERN, Geneva, Switzerland
Higgs boson – “God particle”? – mass 1.25x1011 eV, neither matter nor force!
15 October 1991 Dugway Proving Ground, Utah, U.S.A.
“Oh-my-God-particle”!
(kinetic) energy 3x1020 eV
(=3x1011 GeV = 300 EeV)!

## Slide 67: cosmic-ray energy spectrum
P. Blasi, UHECR2012
1045 m-2s-1sr-1GeV1.5!
LHC p energy
x108
GZK limit
FCC-hh
circular crystal collider

## Slide 68: cosmic-ray energy spectrum
P. Blasi, UHECR2012
1045 m-2s-1sr-1GeV1.5!
LHC p energy
x108
GZK limit
dielectric & plasmas
crystal accelerator driven by X-ray laser

## Slide 69: ultimate limit of electromagnetic acceleration
Ecr ≈1018 V/m critical field for e+e-
pair creation - ħ/(mec) e Ecr ~ mec2
reaching Planck scale of 1028 eV
would need 1010 m long accelerator
[1010 m= 1/10th of distance earth-sun]
“not an inconceivable task for an
advanced technological society”
P. Chen, R, Noble, SLAC-PUB-7402, April 1998

## Slide 70: Summary
bright future for accelerator-based HEP!
HL-LHC prepares FCC technology
Channeling conferences look beyond
several different routes to 10-TeV/100-TeV &
1 PeV collisions
e.g. linear path: ILC→CLIC →DWAC→ XRCMC
circular path: FCC-ee→FCC-hh→CCC
crystals are key for both:
bending and/or acceleration
eventually outer-space solar-system
accelerator needed to reach Planck mass

## Slide 71
“A circle is a round straight line with a hole in the middle.”
  Mark Twain,
  in "English as She Is Taught",
  Century Magazine, May 1887
is future circular or linear or both?

## Slide 72
First FCC Week
Conference
Washington DC
23-27 March 2015
http://cern.ch/fccw2015

## Slide 73: spare slides

## Slide 74
with emphasis on proton-proton and electron-positron high-energy frontier machines.
These design studies should be coupled to a vigorous accelerator R&D programme, including high-field magnets and high-gradient accelerating structures,
in collaboration with national institutes, laboratories and universities worldwide.
http://cds.cern.ch/record/1567258/files/esc-e-106.pdf
….“to propose an ambitious post-LHC accelerator project at CERN by the time of the next Strategy update”:
d) CERN should undertake design studies for accelerator projects in a global context,
European Strategy Update 2013
Design studies and R&D at the energy frontier
strategy adopted at Brussels in May 2013, during exceptional session of the CERN Council in presence of the European Commission

## Slide 75
Cms energy |  |  | 
Luminosity |  |  | 
parameter | LHC | HL-LHC | FCC-hh
c.m. energy [TeV] | 14 |  | 100
dipole magnet field [T] | 8.33 |  | 16 (20)
circumference [km] | 26.7 |  | 100 (83)
luminosity [1034 cm-2s-1] | 1 | 5 | 5 [→20?]
bunch spacing [ns] | 25 |  | 25 (5)
events / bunch crossing | 27 | 135 | 170 (34)
bunch population [1011] | 1.15 | 2.2 | 1 (0.2)
norm. transverse emitt. [mm] | 3.75 | 2.5 | 2.2 (0.44)
IP beta-function [m] | 0.55 | 0.15 | 1.1
IP beam size [mm] | 16.7 | 7.1 | 6.8 (3)
synchrotron rad. [W/m/aperture] | 0.17 | 0.33 | 28 (44)
critical energy [keV] | 0.044 |  | 4.3 (5.5)
total syn.rad. power [MW] | 0.0072 | 0.0146 | 4.8 (5.8)
longitudinal damping time [h] | 12.9 |  | 0.54 (0.32)

## Slide 76: FCC-hh as heavy-ion collider
 | Unit | LHC Design | FCC-hh | FCC-hh
operation mode | - | Pb-Pb | Pb-Pb | p-Pb
number of bunches |  | 592 | 432 | 432
part. / bunch | [108] | 0.7 | 1.4 | 115(1.4)/1.4
β-functionat IP | [m] | 0.5 | 1.1 | 1.1
RMS beam size at IP | [um] | 15.9 | 8.8 | 8.8
initial luminosity | [1027cm-2s-1] | 1 | 3.2 | 267(3.2)
peak luminosity | [1027cm-2s-1] | 1 | 12.7 | 5477(3356)
integr. lumi. per fill | [mb-1] | <15 | 83 | 30240
total cross-section | [b] | 515 | 597 | 2
initial luminosity lifetime | [h] | <5.6 | 3.7 | 3.2 (10.6)
M. Schaumann, J. Jowett
preliminary parameters

## Slide 77
parameter | LEP2 | FCC-ee |  |  |  |  | CepC
 |  | Z | Z (c.w.) | W | H | t | H
Ebeam [GeV] | 104 | 45 | 45 | 80 | 120 | 175 | 120
circumference [km] | 26.7 | 100 | 100 | 100 | 100 | 100 | 54
current [mA] | 3.0 | 1450 | 1431 | 152 | 30 | 6.6 | 16.6
PSR,tot [MW] | 22 | 100 | 100 | 100 | 100 | 100 | 100
no. bunches | 4 | 16700 | 29791 | 4490 | 1360 | 98 | 50
Nb [1011] | 4.2 | 1.8 | 1.0 | 0.7 | 0.46 | 1.4 | 3.7
ex [nm] | 22 | 29 | 0.14 | 3.3 | 0.94 | 2 | 6.8
ey [pm] | 250 | 60 | 1 | 1 | 2 | 2 | 20
b*x [m] | 1.2 | 0.5 | 0.5 | 0.5 | 0.5 | 1.0 | 0.8
b*y [mm] | 50 | 1 | 1 | 1 | 1 | 1 | 1.2
s*y [nm] | 3500 | 250 | 32 | 130 | 44 | 45 | 160
sz,SR [mm] | 11.5 | 1.64 | 2.7 | 1.01 | 0.81 | 1.16 | 2.3
sz,tot [mm] (w beamstr.) | 11.5 | 2.56 | 5.9 | 1.49 | 1.17 | 1.49 | 2.7
hourglass factor Fhg | 0.99 | 0.64 | 0.94 | 0.79 | 0.80 | 0.73 | 0.61
L/IP [1034 cm-2s-1] | 0.01 | 28 | 212 | 12 | 6 | 1.7 | 1.8
tbeam [min] | 300 | 287 | 39 | 72 | 30 | 23 | 40

## Slide 78
collider parameters | FCC ERL | FCC-ee ring |  | protons
species | e- (e+?) | e± | e± | p
beam energy [GeV] | 60 | 60 | 120 | 50000
bunches / beam | - | 10600 | 1360 | 10600
bunch intensity [1011] | 0.05 | 0.94 | 0.46 | 1.0
beam current [mA] | 25.6 | 480 | 30 | 500
rms bunch length [cm] | 0.02 | 0.15 | 0.12 | 8
rms emittance [nm] | 0.17 | 1.9 (x) | 0.94 (x) | 0.04 [0.02 y]
bx,y*[mm] | 94 | 8, 4 | 17, 8.5 | 400 [200 y]
sx,y* [mm] | 4.0 | 4.0, 2.0 |  | equal
beam-b. parameter x | (D=2) | 0.13 | 0.13 | 0.022 (0.0002)
hourglass reduction | 0.92 (HD=1.35) | ~0.21 | ~0.39 | 
CM energy [TeV] | 3.5 | 3.5 | 4.9 | 
luminosity[1034cm-2s-1] | 1.0 | 6.2 | 0.7 | 
preliminary FCC-he parameters shown at ICHEP’14

## Slide 79
International Linear Collider (ILC) - 2
Japanese HEP community expressed interest in hosting the ILC. Site chosen: 北上市 (Kitakami) in Northern Japan. Now 2-year review process by Japanese MEXT.