## Slide 1
Future Circular Collider
Frank Zimmermann for the FCC collaboration
Future Research Infrastructures – Challenges and Opportunities
Varenna, 9 July 2015
Work supported by the European Commission under Capacities 7th Framework Programme projest EuCARD-2, Grant Agreement 312453, and the HORIZON 2020 project EuroCirCol, Grant Agreement 654305
gratefully acknowledging input
from Michael Benedikt & Johannes Gutleber
Photo: courtesy J. Wenninger

## Slide 2
1983 first LHC proposal, launch of design study
1994 CERN Council: LHC approval
2010 first collisions at 3.5 TeV beam energy
2015 collisions at design energy (plan)
now is the time to plan for 2040!
LHC history

## Slide 3
a very large circular hadron collider seems the only approach to reach 100 TeV c.m. range in coming decades
access to new particles (direct production) in the few TeV to 30 TeV mass range, far beyond LHC reach
much-increased rates for phenomena in the sub-TeV mass range → increased precision w.r.t. LHC and possibly ILC
physics motivation for hadron collider:
pushing the energy frontier
the name of the game of a hadron collider is energy reach
cf. LHC: factor 4 in radius, factor 2 in field  factor 10 in Ec.m.
M. Mangano

## Slide 4
European Strategy for Particle Physics 2013:
  “…to propose an ambitious post-LHC accelerator project….., CERN should undertake design studies for accelerator projects in a global context,…with emphasis on proton-proton and electron-positron high-energy frontier machines..…”
US P5 recommendation 2014:
  ”….A very high-energy proton-proton collider is the most powerful tool for direct discovery of new particles and interactions under any scenario of physics results that can be acquired in the P5 time window….”
strategic motivation
ICFA statement 2014:
  ”…. ICFA supports studies of energy frontier circular colliders and encourages global coordination.….”

## Slide 5
international FCC collaboration to study:
pp-collider (FCC-hh)  main emphasis, defining infrastructure requirements
80-100 km infrastructure in Geneva area
e+e- collider (FCC-ee) as potential intermediate step
p-e (FCC-he) option
~16 T  100 TeV pp in 100 km
Future Circular Collider Study
GOAL: CDR and cost review for the next ESU (2018)

## Slide 6
CepC/SppC study (CAS-IHEP) 50-70 km
e+e- collisions ~2028; pp collisions ~2042
Qinhuangdao (秦皇岛）
50 km
70 km
easy access
300 km from Beijing
3 h by car
1 h by train
Yifang Wang
CepC, SppC
“Chinese Toscana”

## Slide 7
H. Ulrich Wienands, The SSC Low Energy Booster: Design and Component Prototypes for the First Injector Synchrotron, IEEE Press, 1997
ex. SSC
Supercolliders Superdetectors: Proceedings of the 19th and 25th Workshops of the INFN Eloisatron Project
ex. ELOISATRON
SSC CDR 1986
ex. TRISTAN II
VLHC Design Study Group Collaboration
June 2001. 271 pp.
SLAC-R-591, SLAC-R-0591, SLAC-591,
SLAC-0591, FERMILAB-TM-2149
http://www.vlhc.org/
ex. VLHC
Tristan-II
option 2
F. Takasaki,
1983
Tristan-II
option 1
Previous studies in Italy (ELOISATRON 300km), USA (SSC 87km, VLHC 233km), Japan (TRISTAN-II 94km)
many aspects of machine design and R&D non-site specific.
exploit synergies with other projects and previous studies

## Slide 8
high energy
  high field superconducting magnets
  large tunnel infrastructures
high luminosity
  beam optics
  beam current
  synchrotron radiation impacting SC magnets
  IR shielding and component lifetime
high stored beam energy
  machine protection
  beam handling
  beam injection and beam dumping
key challenges for FCC-hh/SppC

## Slide 9
FCC-hh: 100 TeV pp collider as long-term goal  defines infrastructure needs
FCC-ee: e+e- collider, potential intermediate step
FCC-he: integration aspects of pe collisions
Tunnel infrastructure in Geneva area, linked to CERN accelerator complex
Site-specific, requested by European strategy
Push key technologies in dedicated R&D programmes e.g.
16 Tesla magnets for 100 TeV pp in 100 km
SRF technologies and RF power sources
FCC Study Scope:
Accelerator and Infrastructure

## Slide 10
Elaborate and document
- Physics opportunities
- Discovery potentials
Experiment concepts for hh, ee and he
Machine Detector Interface studies
Concepts for worldwide data services
Overall cost model
Cost scenarios for collider options
Including infrastructure and injectors
Implementation and governance models
FCC Scope: Physics & Experiments

## Slide 11
FCC-hh parameters
parameter | FCC-hh |  | LHC | HL LHC
c.m. energy [TeV] | 100 |  | 14 | 
dipole field [T] | 16 |  | 8.3 | 
# interaction points (IPs) | 2 main & 2 |  | 2 main & 2 | 
bunch intensity [1011] | 1 | 1 (0.2) | 1.1 | 2.2
bunch spacing [ns] | 25 | 25 (5) | 25 | 25
luminosity/IP [1034 cm-2s-1] | 5 | 20 | 1 | 5
events/bunch crossing | 170 | 680 (136) | 27 | 135
stored energy/beam [GJ] | 8.4 |  | 0.36 | 0.7
synchr. rad. [W/m/aperture] | 30 |  | 0.2 | 0.35

## Slide 12
100 km layout for FCC-hh
(different sizes under investigation)
two high-luminosity experiments (A and G)
two other experiments (F and H)
two collimation straights
two injection and two extraction straights
orthogonal functions for each insertion section
FCC-hh preliminary layout

## Slide 13
90 – 100 km fits geological situation well
LHC suitable as potential injector
site study - 93 km example
J. Osborne, C. Cook, et al.

## Slide 14
increase critical current density
obtain high quantities at required quality
material Processing
reduce cost
develop 16T short models
field quality and aperture
optimum coil geometry
manufacturing aspects
cost optimisation
Conductor R&D
Nb3Sn
Magnet Design
16 T
key technology R&D – high field magnets

## Slide 15
Main Milestones of the FCC Magnets Technologies |  |  |  |  |  |  |  |  |  |  |  |  | 
Milestone | Description | 15 | 2016 |  | 2017 |  | 2018 |  | 2019 |  | 2020 |  | 21
M0 | Supporting wound conductor program |  |  |  |  |  |  |  |  |  |  |  | 
M1 | Design of an RMM with existing wire |  |  |  |  |  |  |  |  |  |  |  | 
M2 | Manufacture and test of a first 16T RMM |  |  |  |  |  |  |  |  |  |  |  | 
M3 | Procurement 35 km state of the art high Jc wire |  |  |  |  |  |  |  |  |  |  |  | 
M4 | Design of a 16T demonstrator with above wire |  |  |  |  |  |  |  |  |  |  |  | 
M5 | Manufacture and test of the 16T demonstrator |  |  |  |  |  |  |  |  |  |  |  | 
M6 | Procurement 70 km of enhanced high Jc wire |  |  |  |  |  |  |  |  |  |  |  | 
M7 | EuroCirCol design 16T accelerator quality model |  |  |  |  |  |  |  |  |  |  |  | 
 | Manufacture and test of the EuroCirCol model |  |  |  |  |  |  |  |  |  |  |  | 
FCC Magnet Technology Program

## Slide 16
  stored beam energy: 8 GJ/beam (0.4 GJ LHC) = 16 GJ total
   equivalent to an Airbus A380 (560 t) at full speed (850 km/h)
  collimation, beam loss control, radiation effects: important
  injection/dumping/beam transfer: critical operations
  magnet/machine protection: to be considered early on
FCC-hh: some design challenges

## Slide 17
high synchrotron radiation load (SR) of protons @ 50 TeV:
~30 W/m/beam (@16 T)
5 MW total in arcs
(LHC <0.2W/m)
beam screen to capture SR and “protect” cold mass
power mostly cooled at beam screen temperature
only fraction reaches magnets at 2 – 4 K
→ optimization of temperature, space, vacuum, impedance, e-cloud, etc.
Synchrotron radiation/beam screen
D. Schulte

## Slide 18
P. Lebrun, L. Tavian
contributions: beam screen (BS) & cold bore (BS heat radiation)
At 1.9 K cm optimum BS temperature range: 50-100 K;
but impedance increases with temperature  instabilities
40-60 K favoured by vacuum & impedance considerations
 100 MW refrigerator power on cryo plant
cryo power for cooling of SR heat
Contributions to cryo load:
beam screen (BS) &
cold bore (BS heat radiation)
At 4.5 K cold bore, one could potentially increase beam-screen temperature and lower refrigerator power to 50 MW.

## Slide 19
new type of ante-chamber
absorption of synchrotron radiation
avoids photo-electrons
helps beam vacuum
Heat transport
Vacuum quality
Photon distribution
R. Kersevan,
C. Garion,
L. Tavian, et al.
novel beam screen - design example

## Slide 20
Two parameter sets for two operation phases:
  Phase 1 (baseline): 5 x 1034 cm-2s-1 (peak), 250 fb-1/year (averaged)
    2500 fb-1 within 10 years (~HL LHC total luminosity)
  Phase 2 (ultimate): 2.5 x 1035 cm-2s-1 (peak), 1000 fb-1/year (averaged)
   15,000 fb-1 within 15 years
  Yielding total luminosity O(20,000) fb-1
  over 25 years of operation
FCC-hh luminosity goals & phases

## Slide 21
20 ab-1 OK for physics

## Slide 22
phase 1: b*=1.1 m, DQtot=0.01, tta=5 h
phase 2: b*=0.3 m, DQtot=0.03, tta=4 h
  for both phases:
  beam current 0.5 A unchanged!
  total synchrotron radiation power 5 MW.
radiation damping: t1 h
luminosity evolution over 24 h

## Slide 23
integrated luminosity / day
phase 1: b*=1.1 m, DQtot=0.01, tta=5 h
phase 2: b*=0.3 m, DQtot=0.03, tta=4 h

## Slide 24
LEP – highest energy e+e- collider so far
circumference 27 km
in operation from 1989 to 2000
maximum c.m. energy 209 GeV
maximum synchrotron radiation power 23 MW

## Slide 25: physics requirements for FCC-ee
highest possible luminosity
beam energy range from 35 GeV to 200 GeV
physics programs / energies:
  aQED (35 GeV): running coupling constant close to the Z pole ?
  Z (45.5 GeV): Z pole, ‘TeraZ’ and high precision MZ & GZ
  H (63 GeV): H production in s channel (w. mono-chromatization) ??
  W (80 GeV): W pair production threshold, high precision MW
  H (120 GeV): ZH production (maximum rate of H’s)
  t (175 GeV): threshold
  >175 GeV: physics ??
some polarization up to ≥80 GeV for beam energy calibration
optimized for operation at 120 GeV?! (2nd priority “Tera-Z”)
A. Blondel, P. Janot, et al.

## Slide 26: luminosity vs c.m. energy
Z
WW
HZ
H?
aQED
?

## Slide 27: key parameters FCC-ee
parameter | FCC-ee |  |  | LEP2
energy/beam [GeV] | 45 | 120 | 175 | 105
bunches/beam | 13000- 60000 | 500- 1400 | 51- 98 | 4
beam current [mA] | 1450 | 30 | 6.6 | 3
luminosity/IP x 1034 cm-2s-1 | 21 - 280 | 5 - 11 | 1.5 - 2.6 | 0.0012
energy loss/turn [GeV] | 0.03 | 1.67 | 7.55 | 3.34
synchrotron power [MW] | 100 |  |  | 22
RF voltage [GV] | 0.2-2.5 | 3.6-5.5 | 11 | 3.5
dependency: crab-waist vs. baseline optics and 2 vs. 4 IPs

## Slide 28: SC RF System
RF system requirements are characterized by two regimes:
  high gradients for H and – up to ≈11 GV
  high beam loading with currents of ≈1.5 A at the Z pole
aiming for SC RF cavities with gradients of ≈20 MV/m; lower gradients (e.g. 10-15 MV/m) also acceptable
RF frequency of 400 MHz
conversion efficiency (wall plug to RF power) is important for power consumption - aiming for 75% or higher  R&D !
  important item for FCC-ee power budget, 65% achieved for LEP2
  recent breakthrough in klystron efficiency (I. Syratchev)
J. Wenninger, A. Butterworth, E. Jensen, et al.

## Slide 29: luminosity scaling: larger E & r
H  1
Hour-glass
2F
F  1
Crossing angle
Beam-beam parameter
J. Wenninger

## Slide 30: luminosity scaling: damping
beam-beam parameter x measures strength of field sensed by the particles in a collision
beam-beam parameter limits are empirically scaled from LEP data (4 IPs)
In reasonable agreement with first simulations for FCC ee
J. Wenninger, R. Assmann, S. White, K. Ohmi, D. Shatilov, et al.
R. Assmann & K. Cornelis, EPAC2000
x4
x4.5
x1/50
<x2
FCC-ee
vs LEP
extremely high luminosity

## Slide 31: beam-beam simulations
K. Ohmi, D. Shatilov
The beam-beam limit may further be raised with crab-waist schemes !
analytical estimates confirmed by the simulations

## Slide 32
crab-waist crossing for flat beams
regular crossing
crab waist -
vertical waist position
in s varies with horizontal
position x
allows for small by*
and avoids betatron resonances
P. Raimondi,
et al. (SuperB, DAFNE)

## Slide 33: beamstrahlung – a new limit at 175 GeV
hard photon emission at the IPs, ‘Beamstrahlung’, can become lifetime / performance limit for large bunch populations (N), small hor. beam size (sx) & short bunches (ss)
r : mean bending radius at the IP (in the field of the opposing bunch)
for acceptable lifetime, rh must be sufficiently large
  flat beams (large sx) !
  bunch length !
  large momentum acceptance: ≥1.5% at 175 GeV
    - LEP: <1% acceptance, SuperKEKB ~ 1.5%
h : ring energy acceptance
g
e
e
lifetime expression by V. Telnov, modified version by A. Bogomyagkov et al
J. Wenninger, et al

## Slide 34: SuperKEKB = FCC-ee demonstrator
beam commissioning will start in 2015
top up injection at high current
by* =300 mm (FCC-ee: 1 mm)
lifetime 5 min (FCC-ee: ≥20 min)
ey/ex =0.25% (similar to FCC-ee)
off momentum acceptance (±1.5%, similar to FCC-ee)
e+ production rate (2.5x1012/s, FCC-ee: <1.5x1012/s (Z crab waist)
SuperKEKB goes beyond FCC-ee, testing all concepts
K. Oide et al.

## Slide 35: by* evolution over 40 years
year
b* [m]
SuperKEKB
FCC-ee
PETRA
SPEAR
PEP, BEPC, LEP
CESR
DORIS
TRISTAN
DAFNE
CESR-c, PEP-II
KEKB
BEPC-II
6 mm
1 mm
0.3 mm
entering a new regime for ring colliders –
SuperKEKB will pave the way towards b*≤1 mm

## Slide 36: FCC-ee injection
beside the collider ring(s), a booster of the same size (same tunnel) must provide beams for top-up injection
  same size of RF system, but low power (~ MW)
  top up frequency ≈0.1 Hz
  booster injection energy ≈20 GeV
  bypass around the experiments
injector complex for e+ and e- beams of 10-20 GeV
  Super-KEKB injector ≈ almost suitable
A. Blondel

## Slide 37: top-up injection at PEP-II
Before Top-Up
After Top-Up
average luminosity ≈ peak luminosity
J. Seeman
similar results from KEKB

## Slide 38: FCC-ee top-up
two new options for top-up:
off-momentum multipole kicker injection
or kicker-less (“dream injection”)
Wire septum
Injection point (d=-4%)
2nd turn (d~-3%)
M. Aiba, A. Saa Hernandez, PSI
*
* earlier proposal by R. Talman

## Slide 39: IR optics with crab waist and solenoids
these sextupoles work as crab waist sextupoles
K. Oide

## Slide 40: complete draft optics & geometry for FCC-ee
asymmetric layout -
less bending for incoming beam, stronger bending for outgoing beam; reduced synchrotron radiation towards the IP
K. Oide
a bypass for the injector?

## Slide 41: dynamic aperture
±2%
K. Oide

## Slide 42: FCC-he baseline: linac-ring collider
luminosity of LR collider:
highest proton
beam brightness
available
smallest possible
proton b* function:
reduced l*
squeeze only
one p beam
maximize geometric
overlap factor
head-on collision
small e- emittance
qc=0
Hhg≥0.7
(round beams)
average e-
current
limited by
energy
recovery
efficiency
Ie=25.6 mA (LHeC-HF)
HD~1.3
D. Schulte
LHeC2010

## Slide 43: one option: reuse the LHeC
gap turn 1
gap turn 2
gap turn 3
gap turn 1
gap turn 2
gap turn 3
CLHeC=CLHC/n
future: CLHeC=pCFCC/m
IP#1
IP#2
DC=k CLHeC
LHC
FCC
m, n (=3 or 4), k: integer
p = 1 or 2

## Slide 44: LHeC HF → FCC-he (FCC-hh phase 2)
parameter [unit] |  | FCC-hh
species | e- | p
beam energy (/nucleon) [GeV] | 60 | 7000→ 50000
bunch spacing [ns] | 25 | 25
bunch intensity (nucl,) [1010] | 0.4 | 22→ 10
beam current [mA] | 25.6 | 1110 → 500
normalized rms emittance [mm] | 20 → 10 | 2.5 → 0.75
geometric rms emittance [nm] | 0.17→0.085 | 0.34 → 0.014
IP beta function bx,y* [m] | 0.10→0.048 | 0.05 → 0.3
IP rms spot size [mm] | 4.1 → 2.0 | 4.1 →2.0
lepton D & hadron x | 23 → 48 | 0.0002→0.0007
hourglass reduction factor Hhg | 0.80→ 0.80 | 
pinch enhancement factor HD | ~1.35 | 
luminosity/nucl. [1033cm-1s-1] | 14.4 → 27.6 | 

## Slide 45
h-e Higgs-boson production and decay; and precision measurements of the H–bb coupling in WW–H production; FCC-he also gives access to Higgs self-coupling H–HH (<10% precision!? - under study), to lepto-quarks up to ≈4 TeV & to Bjorken x as low as 10-7 - 10-8 [of interest for ultra high energy n scattering]
Higgs physics at FCC-he
M. Klein and H. Schopper, CERN Courier June2014

## Slide 46
Constr.
Physics
LEP
Construction
Physics
Proto
Design
LHC
Construction
Physics
Design
HL-LHC
Physics
Construction
Proto
Design
FCC
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
2030
2035
20 years
CERN Circular Colliders + FCC

## Slide 47
2014 |  |  |  | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
Explore options
“weak interaction”
Report
Study plan, scope definition
FCC Week 2018
 contents of CDR
CDR ready
FCC Week 2015:
work towards baseline
conceptual study of baseline “strong interact.”
FCC Week 17 & Review Cost model, LHC results  study re-scoping?
Elaboration,
consolidation
FCC Week 2016
Progress review
Study time line towards FCC CDR

## Slide 48: FCC Collaboration Status
58 institutes
22 countries + EC

## Slide 49
FCC Collaboration Status
58 collaboration members & CERN as host institute, 8 July 2015
ALBA/CELLS, Spain
Ankara U., Turkey
U Belgrade, Serbia
U Bern, Switzerland
BINP, Russia
CASE (SUNY/BNL), USA
CBPF, Brazil
CEA Grenoble, France
CEA Saclay, France
CIEMAT, Spain
CNRS, France
Cockcroft Institute, UK
U Colima, Mexico
CSIC/IFIC, Spain
TU Darmstadt, Germany
DESY, Germany
TU Dresden, Germany
Duke U, USA
EPFL, Switzerland
GWNU, Korea
U Geneva, Switzerland
Goethe U Frankfurt, Germany
GSI, Germany
Hellenic Open U, Greece
HEPHY, Austria
U Houston, USA
IFJ PAN Krakow, Poland
INFN, Italy
INP Minsk, Belarus
U Iowa, USA
IPM, Iran
UC Irvine, USA
Istanbul Aydin U., Turkey
JAI/Oxford, UK
JINR Dubna, Russia
FZ Jülich, Germany
KAIST, Korea
KEK, Japan
KIAS, Korea
King’s College London, UK
KIT Karlsruhe, Germany
Korea U Sejong, Korea
MEPhI, Russia
MIT, USA
NBI, Denmark
Northern Illinois U., USA
NC PHEP Minsk, Belarus
U. Liverpool, UK
U Oxford, UK
PSI, Switzerland
Sapienza/Roma, Italy
UC Santa Barbara, USA
U Silesia, Poland
TU Tampere, Finland
TOBB, Turkey
U Twente, Netherlands
TU Vienna, Austria
Wroclaw UT, Poland

## Slide 50
Core aspects of hadron collider design: arc & IR optics design, 16 T magnet program, cryogenic beam vacuum system
Recognition of FCC Study by European Commission
EC contributes with funding to FCC-hh study
EuroCirCol EU Horizon 2020 Grant

## Slide 51: EuroCirCol Consortium + Associates
Japan
KEK
Finland
TUT
France
CEA, CNRS
Italy
INFN
Germany
KIT, TUD
Switzerland
EPFL, UNIGE
Netherlands
UT
Spain
ALBA, CIEMAT
CERN
United Kingdom
STFC, UNILIV, UOXF
CERN | IEIO
TUT | Finland
CEA | France
CNRS | France
KIT | Germany
TUD | Germany
INFN | Italy
UT | Netherlands
ALBA | Spain
CIEMAT | Spain
STFC | United Kingdom
UNILIV | United Kingdom
UOXF | United Kingdom
KEK | Japan
EPFL | Switzerland
UNIGE | Switzerland
NHFML-FSU | USA
BNL | USA
FNAL | USA
LBNL | USA
Consortium Beneficiaries, signing the Grant Agreement

## Slide 52
Conclusions
bright future for accelerator-based HEP!
we now need to urgently prepare for post-LHC period
circular hadron collider - only path available in this century towards direct discoveries at 10s of TeV energy
FCC-hh further develops the new Nb3Sn magnet technology of the HL-LHC, it also promotes many other technological innovations (cryogenics, chamber production,…)
FCC-ee: attractive intermediate step towards FCC-hh & highly synergetic (infrastructure, time, physics, + SRF)
FCC-he: complementary physics, extension of LHeC
great worldwide interest - forming global collaboration

## Slide 53
FCC Week 2016
Rome, 11-15 April 2016

## Slide 54: … surely great times ahead!

## Slide 55
spare slides

## Slide 56
Courtesy V. Shiltsev
pp
e+e-
factor 10 every
20-30 years
factor 10 every
10 years
factor 105-107 in e+e-
luminosity
collider c.m. energy vs. year
Ecm=2ec Br
hadron-lepton
FCC-he
LHeC
ep

## Slide 57
FCC-hh: 100 TeV pp collider
LHC
27 km, 8.33 T
14 TeV (c.m.)
FCC-hh (alternative)
80 km, 20 T
100 TeV (c.m.)
FCC-hh (baseline)
100 km, 16 T
100 TeV (c.m.)
“HE-LHC”
27 km, 20 T
33 TeV (c.m.)
Geneva
PS
SPS
LHC
L. Bottura
B. Strauss