## Slide 1: LHC & Future High-Energy Frontier Circular Colliders
Work supported by the European Commission under Capacities 7th Framework Programme, Grant Agreement 312453
Frank Zimmermann, CERN/BE
CINVESTAV Merida
5 September 2013
thanks to R. Aleksan, R. Assmann, A. Blondel,
Y. Cai, O. Dominguez, J. Ellis, B. Holzer, P. Janot,
M. Koratzinos, H. Maury Cuna, S. Myers, K. Ohmi,
K. Oide, J. Osborne, L. Rossi, J. Seeman, V. Telnov,
R. Tomas, U. Wienands, K. Yokoya, M. Zanetti, …

## Slide 2
CERN
“accelerators”
LHC
history, 2010-12 run, next 10 years, HL-LHC
ep & gg Higgs factories: LHeC & SAPPHiRE
in parallel to HL-LHC? preparing for future e+e- H factory
high-energy hadron colliders: HE-LHC & VHE-LHC
sharing tunnel with leptons
circular e+e- Higgs factory: TLEP
long-term strategy
outline

## Slide 3: CERN – The World’s Largest Particle Physics Laboratory
CERN was founded in 1954 with the aim of ‘Science for Peace’
It now has 20 member states – most of europe, with observers including USA and Russia
It employs ~2300 staff, with ~11’000 users, mainly from univiersities and institutes
SPS
Meyrin
Prévessin
CPS
LHC
ALICE
LHC-b
CMS
ATLAS

## Slide 4
Science is getting more and more global
41
Notes: 4
4

## Slide 5: The ‘Standard Model’
We have a model, but it is (was) missing the Higgs Boson
But the Higgs Boson is very heavy, so to discover it, we need a very high energy accelerator

## Slide 6
A standard household power cable will carry 13 Amps of electrical current
13 Amps at room temperature

## Slide 7
To make a magnet strong enough for the LHC in our existing tunnel, we needed 13’000 Amps of current
13 Amps at room temperature
13’000 Amps at room temperature

## Slide 8
Making magnets from superconducting cable, operating at 2 Kelvin (-271 C) was the only way for the LHC
13 Amps at room temperature
13’000 Amps at room temperature
13’000 Amps at 2 Kelvin

## Slide 9
If it used resistive magnets operating at 1.8 T the circumference would have to be about 100 km, and the electrical consumption 900 MW (a good-sized power plant), this cost would be too high, both for the project and for the environment
The LHC has a circumference of 26.7 km, out of which some 20 km is main superconducting magnets providing 8.3 Tesla dipole field. Maintaining this field uses virtually no electrical power.
However, the LHC is not completely free… the cryogenics plant to cool the ~700 m3 of liquid helium needed to keep the magnets at 2 Kelvin will consume about 40 MW electrical power from the mains.

## Slide 13
colliding beams
centre-of-mass energy:
beam hits
a “fixed target”
two beams collide
colliding two beams against each other can provide
much higher centre-of-mass energies than fixed target!

## Slide 14
design parameters
c.m. energy = 14 TeV (p)
luminosity =1034 cm-2s-1
1.15x1011 p/bunch
2808 bunches/beam
360 MJ/beam
ge=3.75 mm
b*=0.55 m
qc=285 mrad
sz=7.55 cm
s*=16.6mm
LHC: highest energy pp, AA, and pA collider

## Slide 15: short LHC history
1983 LEP Note 440 - S. Myers and W. Schnell propose
twin-ring pp collider in LEP tunnel with 9-T dipoles
1991 CERN Council: LHC approval in principle
1992 EoI, LoI of experiments
1993 SSC termination
1994 CERN Council: LHC approval
1995-98 cooperation w.Japan,India,Russia,Canada,&US
2000 LEP completion
2006 last s.c. dipole delivered
2008 first beam
2010 first collisions at 3.5 TeV beam energy
2015 collisions at ~design energy (plan)
>30 years!
now is the time to plan for ~2040

## Slide 16
luminosity
reaction rate
luminosity
R= s L
C. Amsler et al., Physics Letters B667, 1 (2008)
from
cosmic rays
LHC
cross section
tot~
100 mbarn
~ 10-25 cm2
inelastic~
80 mbarn~
8x10-26 cm2

## Slide 17: integrated pp luminosity 2010-12
2010: 0.04 fb-1
  7 TeV CoM
  Commissioning
2011: 6.1 fb-1
  7 TeV CoM
  Exploring the limits
2012: 23.3 fb-1
  8 TeV CoM
  Production
M. Lamont, IPAC’13

## Slide 18: reliable luminosity forecasts

## Slide 19: peak performance through the years
 | 2010 | 2011 | 2012 | Nominal
bunch spacing [ns] | 150 | 50 | 50 | 25
no. of bunches nb | 368 | 1380 | 1380 | 2808
b* [m] ATLAS and CMS | 3.5 | 1.0 | 0.6 | 0.55
max. bunch intensity N [protons/bunch] | 1.2 x 1011 | 1.45 x 1011 | 1.7 x 1011 | 1.15 x 1011
normalized emittance ge [mm-mrad] | ~2.0 | ~2.4 | ~2.5 | 3.75
peak luminosity L [cm-2s-1] | 2.1 x 1032 | 3.7 x 1033 | 7.7 x 1033 | 1.0 x 1034
M. Lamont, IPAC’13
>2x design when scaled to 7 TeV

## Slide 20
20
Huge efforts over last months to prepare for high lumi and pile-up expected in 2012:
optimized trigger and offline algorithms (tracking, calo noise treatment, physics objects)
 mitigate impact of pile-up on CPU, rates, efficiency, identification, resolution
in spite of x2 larger CPU/event and event size  we do not request additional computing
resources (optimized computing model, increased fraction of fast simulation, etc.)
Z μμ
Z μμ event from 2012 data with 25 reconstructed vertices
pile up
will increase
at higher energy
→
experiments
request
25 ns
operation
in 2015
M. Lamont, IPAC’13
event pile up

## Slide 21: ATLAS & CMS pp physics

## Slide 22
The highlight of a remarkable year 2012

## Slide 23: LHCb
luminosity levelling
at around 4e32 cm-2s-1 via transverse separation
ATLAS/CMS
LHCb
first evidence for the decay Bs -> m+ m-
M. Lamont, IPAC’13
beam 1
beam 2

## Slide 24
M. Lamont
LHC injector complex
LHC also provides Pb-Pb (2011) and Pb-p collisions (2013)

## Slide 25: operational cycle
Beam dump
Ramp down/precycle
Injection
Ramp
Squeeze
Collide
Stable beams
Ramp down | 35 mins
Injection | ~30 mins
Ramp | 12 mins
Squeeze | 15 mins
Collide | 5 mins
Stable beams | 0 – 30 hours
turn around 2 to 3 hours on a good day
M. Lamont, IPAC’13

## Slide 26: availability
“There are a lot of things that can go wrong – it’s always a battle”
Pretty good availability considering the complexity and principles of operation
Cryogenics availability in 2012: 93.7%
M. Lamont, IPAC’13

## Slide 27
some issues in 2011-12 operation
UFOs
20 dumps in 2012
time scale 50-200 µs
conditioning observed
worry about 6.5 TeV and 25 ns spacing
Beam induced heating
Local non-conformities (design, installation)
  injection protection devices
  sync. Light mirrors
  vacuum assemblies
Radiation to electronics
“single event upsets”
concerted program of mitigation measures (shielding, relocation…)
premature dump rate down from 12/fb-1 in 2011 to 3/fb-1 in 2012
T. Baer

## Slide 28
another big issue : electron cloud
beam induced multipactoring process, depending on secondary emission yield
LHC strategy based on surface conditioning (scrubbing runs)
worry about 25 ns (more conditioning needed) and 6.5 TeV (photoelectrons)
25-ns scrubbing in 2011 – decrease of SEY
25-ns scrubbing in 2012 – conditioning stop?
G. Iadarola, H. Maury, G. Rumolo
H. Maury Cuna

## Slide 29: Long Shutdown 1 - motivation
after 2008 incident partial consolidation
& problem of imperfect Cu
stabilizer continuity
in 2010-12 LHC operated at 7 & 8 TeV c.m.
beam energy to avoid any risk
presently: Long Shutdown 1 (LS1) ~2 yr
to prepare LHC for 13-14 TeV c.m.,
detector upgrades in parallel

## Slide 30: 2008 “incident”
A faulty bus-bar (SC splice) in a magnet interconnect failed, leading to an electric arc which dissipated some 275 MJ
This burnt through beam vacuum and cryogenic lines, rapidly releasing ~2 tons of liquid helium into the vacuum enclosure
R. Veness

## Slide 34: 2015 – post LS1
energy: 6.5 TeV (magnet retraining)
bunch spacing: 25 ns
  pile-up considerations
injectors potentially able to offer nominal intensity with even lower emittance
 | Number of bunches | Ib LHC FT[1e11] | Emit LHC [um] | Peak Lumi [cm-2s-1] | ~Pile-up | Int. Lumi per year [fb-1]
25 ns low emit | 2520 | 1.15 | 1.9 | 1.7e34 | 52 | ~45
BCMS = Batch Compression and Merging and Splitting
expected maximum luminosity
from inner triplet heat load
(collisions debris) 1.7×10 34 cm-2s-1 ±20%

## Slide 35
uncertainties for 2015:
electron cloud
UFOs
both get more difficult at 25 ns &
at higher energy
energy (limited by retraining)

## Slide 36: example LHC time line – next ten years
Ralph Steinhagen, ICHEP2012

## Slide 37: LHC luminosity forecast
~30/fb at 3.5 & 4 TeV
~400/fb at 6.5-7 TeV
~3000/fb at 7 TeV
to obtain 3000/fb by 2035
we need the HL-LHC
2012 DONE
2021 goal (?)
2035 goal (??)

## Slide 38: HL-LHC – modifications
Booster energy upgrade
1.4 → 2 GeV, ~2018
Linac4,
~2015
SPS enhancements
(anti e-cloud coating?,RF,
impedance), 2012-2022
IR upgrade
(detectors, low-b quad’s, crab cavities, a few high-field dipoles, etc)
~2022
Cristhian Valerio
U. Sinaloa

## Slide 39: in LHC: 1.2 km of new equipment …
6.5 kW@4.5K cryoplant
2 x 18 kW @4.5K cryoplants for IRs

## Slide 40: HL-LHC Official Beam Parameters
Parameter | nominal | 25ns | 50ns
N | 1.15E+11 | 2.2E+11 | 3.5E+11
nb | 2808 | 2808 | 1404
beam current [A] | 0.58 | 1.12 | 0.89
x-ing angle [mrad] | 300 | 590 | 590
beam separation [s] | 10 | 12.5 | 11.4
b* [m] | 0.55 | 0.15 | 0.15
en [mm] | 3.75 | 2.5 | 3.0
eL [eVs] | 2.51 | 2.5 | 2.5
energy spread | 1.20E-04 | 1.20E-04 | 1.20E-04
bunch length [m] | 7.50E-02 | 7.50E-02 | 7.50E-02
IBS horizontal [h] | 106 | 20.0 | 20.7
IBS longitudinal [h] | 60 | 15.8 | 13.2
Piwinski parameter | 0.68 | 3.1 | 2.9
geom. reduction | 0.83 | 0.35 | 0.33
beam-beam / IP | 3.10E-03 | 3.9E-03 | 5.0E-03
Peak Luminosity | 1 1034 | 7.4 1034 | 8.5 1034
Virtual Luminosity | 1.2 1034 | 21 1034 | 26 1034
(Leveled to 5 1034 cm-2 s-1
and 2.5 1034 cm-2 s-1)
Events / crossing (peak & leveled L) | 19 | 210 | 475 | 140 | 140
6.2 1014 and 4.9 1014
p/beam
27

## Slide 41
luminosity leveling at the HL-LHC
example: maximum pile up 140
(sinel~85 mbarn)

## Slide 42
luminosity leveling at the HL-LHC
example: maximum pile up 140

## Slide 43
luminosity & integrated luminosity during 30 h at the HL-LHC
example: maximum pile up 140
~4 fb-1 per day,
with 40% of efficiency
~250 fb-1 /year

## Slide 44: final goal : 3000 fb-1 by 2030’s…
Full project
Enhanced consolidation

## Slide 45
some HL-LHC ingredients
11-T dipoles for dispersion suppressors
Nb3Sn instead of Nb-Ti
provide space for extra
collimators catching off
-energy protons or ions
at ALICE, collimator
sections, ATLAS & CMS
new final quadrupoles
Nb3Sn instead of Nb-Ti
larger aperture
allowing smaller b*
SC link
move radiation
sensitive power
converters away from
machine
first prototype, 20 m – 20 kA, under test at CERN!
also of interest for electrical power distribution
T. Baer
LQS03 (90 mm ap., 3.7 m long):
208 T/m@4.6 K, 210 T/m@1.9 K
HQ02a (120 mm, 1.5 m long):
150 T/m@4.6 K, 170 T/m@1.9 K
Goal: 150 mm ap, 140 T/m
June 2013
1-m model tested in April 2013,
Bnom=11 T achieved!
Next: 2-m single bore, then 2-in-1
tests of novel MgB2 and HTS (YBCO and BSCCO) cables

## Slide 46
luminosity reduction factor
nominal
LHC
~1/b*
HL-LHC
“Piwinski angle”
luminosity reduction due to crossing angle
is more pronounced at smaller b*
crab cavities
qc/2
eff. beam size:
s*x,eff ≈ sx*/Rq

## Slide 47
schematic of crab crossing
qc
RF crab cavity deflects head and tail in opposite direction so that collision is effectively “head on” for luminosity and tune shift
bunch centroids still cross at an angle (easy separation)
1st proposed in 1988, used in operation at KEKB since 2007
until recently plan was to vary crab cavity voltage for leveling, but this would change
size of luminous region & is disliked by experiments (instead leveling by b* or offset?)

## Slide 48
Final down-selected compact cavity designs for the LHC upgrade: 4-rod cavity design by Cockcroft I. & JLAB (left), l/4 TEM cavity by BNL (centre), and double-ridge l/2 TEM cavity by SLAC & ODU (right).
Prototype compact Nb-Ti crab cavities for the LHC: 4-rod cavity (left) and double-ridge cavity (right).
HL-LHC needs compact crab cavities
only 19 cm beam separation, but long bunches

## Slide 49: PoP double-ridge cavity achieved 7 MV deflecting voltage cw in 1st attempt
Expected
Q0 = 6.7×109
  At RS = 22 nΩ
  And Rres = 20 nΩ
Achieved
Q0 = 4.0×109
Achieved fields
  ET = 18.6 MV/m
  VT = 7.0 MV
  EP = 75 MV/m
  BP = 131 mT
Quench
4.2 K
2.0 K
HL-LHC goal:
3.3 MV in operation
better than required!
J. Delayen
S. De Silva
et al -
ODU,
SLAC,
JLAB,
Niowave
J. Delayen, LARP CM20
B. Yee Rendon, CiINVESTAV Mexico

## Slide 50: HL-LHC preliminary budget estimate
 | Improving Consolidation | Full performance | Total HL-LHC
Mat. (MCHF) | 476 | 360 | 836
Pers. (MCHF) | 182 | 31 | 213
Pers. (FTE-y) | 910 | 160 | 1070
TOT (MCHF) | 658 | 391 | 1,049

## Slide 51
RLIUP 2013
“Review of LHC and injector upgrade plans”
CERN, October 2013
3 scenarios | PICs Performance Improving Consolidations | US1 Upgrade Scenario 1 | US2 Upgrade Scenario 2
 |  | +HHRF?+DS collimators? | +crab cavities, e-lens,…
integrated luminosity by 2035 | 1000-1200/fb | 2000/fb | 3000/fb
physics needs & motivation?; also, reasons to go >3000/fb?

## Slide 53
ERL LHeC:
recirculating
linac with
energy
recovery
Large Hadron electron Collider (LHeC)

## Slide 54
~600 pages
LHeC Conceptual Design Report
LHeC CDR published in
J. Phys. G: Nucl. Part. Phys. 39
075001 (2012)

## Slide 55: LHeC ERL layout
two SC linacs, 3-pass up, 3-pass down; 6.4-mA 60-GeV e-’s collide w. LHC p/ions, e- RF grad ~20 MV/m, 800 MHz
(C=1/3 LHC allows for ion clearing gaps)
A. Bogacz, O. Brüning,
M. Klein, D. Schulte,
F. Zimmermann, et al

## Slide 56
LHeC SRF & ERL test facility
design under study

## Slide 57
LHeC baseline & Higgs factory parameters
Lep ~2 1034 cm-2s-1

## Slide 58
SAPPHiRE

## Slide 59
s-channel production;
lower energy;
no e+ source
gg collider Higgs factory
few J pulse
energy with
l~350 nm
Source: Fiber lasers and amplifiers: an ultrafast performance evolution, Jens Limpert, Thomas Schreiber, and Andreas Tünnermann, Applied Optics, Vol. 49, No. 25 (2010)
power evolution of cw double-clad fiber lasers with diffraction limited beam quality over the past decade: factor 100 increase!
K. Moenig et al, DESY Zeuthen
passive optical cavity → relaxed laser parameters
physics
IR
laser
optical cavity

## Slide 60
SAPPHiRE gg Higgs Factory
SAPPHiRE: Small Accelerator for Photon-Photon Higgs production using Recirculating Electrons
scale ~ European XFEL,
about 10-20k Higgs per year
Reconfigured LHeC

## Slide 61
Y. Zaouter, Amplitude Systems
J. Gronberg, LLNL
laser options for SAPPHiRE
G. Mourou, LOA;
M. Velasco,
Northwestern U.
10 J at 10 kHz
EuCARD SAPPHiRE Day 19 February 2013
full power
w/o optical
cavity!
industry
Livermore
ICAN

## Slide 62
LHeC Higgs factory comparison
(1 year = 107 s at design luminosity).
machine | LHeC | LHeC-HF | SAPPHiRE
luminosity [1034 cm-2s-1] | 0.1 (ep) | 2 (ep) | 0.06 (gg >125 GeV)
cross section | ~200 fb | ~200 fb | >1.7 pb
no. Higgs/yr | 2k | 40k | >10k

## Slide 63
higher-energy
pp colliders

## Slide 64: circular pp Higgs factories
LHC: 1st circular Higgs factory!
ECM=8-14 TeV,1034cm-2s-1
HL-LHC: planned (~2022-2035):
ECM=14 TeV,5x1034cm-2s-1 (leveled)
HE-LHC: proposed in LHC tunnel (2038-?)
ECM=33 TeV,x1034cm-2s-1
or
VHE-LHC: proposed in new 80-100 km tunnel (2040?)
ECM=84-104 TeV,x1034cm-2s-1
THE ultimate Higgs factory!
1 M Higgs produced so far – more to come!
15 H bosons / min – and more to come
10x more Higgs
6x higher cross section
for H self coupling
42x higher cross section
for H self coupling

## Slide 65: High-Energy LHC
2-GeV Booster
Linac4
S-SPS?
HE-LHC
20-T dipole magnets
higher energy
transfer lines

## Slide 66
E. Todesco, L. Rossi, P.. McIntyre
20-T dipole magnet
beam
pipe

## Slide 67: VHE-LHC
VHE-LHC
VHE-LHC-LER

## Slide 68
80 or 100-km tunnel for VHE-LHC
J. Osborne, C. Waaijer,
CERN, ARUP & GADZ
the same tunnel could host an e+e- Higgs factory “TLEP” and a highest-luminosity highest-energy e-p/A collider

## Slide 69
parameter | LHC | HL-LHC | HE-LHC | VHE-LHC
c.m. energy [TeV] | 14 | 14 | 33 | 100
circumference [km] | 26.7 | 26.7 | 26.7 | 80 (or 100)
dipole field [T] | 8.33 | 8.33 | 20 | 20 (or 16)
beam current [A] | 0.58 | 1.12 | 0.48 | 0.49
rms IP spot size [mm] | 16/7 | 7.1 (min) | 5.2 | 6.7
stored beam energy [MJ] | 362 | 694 | 701 | 6610
SR power per ring [kW] | 3.6 | 7.3 | 96.2 | 2900
arc SR heat load [W/m/apert.] | 0.17 | 0.33 | 4.35 | 43.4
energy loss per turn [keV] | 6.7 | 6.7 | 201 | 5857
critical photon energy [eV] | 44 | 44 | 575 | 5474
longit. SR emit. damping time [h] | 12.9 | 12.9 | 1.03 | 0.32
peak events / crossing | 27 | 135 (lev.) | 147 | 171
peak luminosity [1034 cm-2s-1] | 1.0 | 5.0 | ≥5.0 | ≥5.0
beam lifetime due to burn off [h] | 45 | 15.4 | 5.7 | 14.8
optimum av. luminosity / day [fb-1] | 0.5 | 2.8 | 1.4 | 2.1
HE-LHC & VHE-LHC parameters
O. Dominguez,
L. Rossi, F. Zimmermann

## Slide 70
SR damping counteracted by transverse + longit. noise injection (constant tune shift & bunch length)
VHE-LHC: time evolution over 11 h in physics
with p burn off & controlled blow up
emittances
luminosity
& bunch intensity
O. Dominguez
HE-LHC &VHE-LHC luminosities could greatly improve for bunch spacings < 25 ns, e.g. by factor 5 for 5 ns, making better use of strong radiation damping!
are 5 ns spacing & 2.5x1035cm-2s-1 acceptable for detectors?

## Slide 71: circular e+e- Higgs factories
2012 - LHC discovered Higgs boson at 126 GeV
cross section for H production in e+e- collisions maximum at ~15% higher beam energy than LEP2
circular collider (“TLEP”) in new 80-100 tunnel: 300x LEP2 luminosity at 4 IPs (precision H studies)
recipe for high luminosity: smaller b* (esp. y), lower emittance (x & y), top-up injection
operation up to threshold; very high luminosity at Z pole & WW threshold (+ polarized beams!)
in same tunnel: pp collider up to 100-TeV c.m. (VHE-LHC), and ep collider
TLEP will enhance VHE-LHC physics case

## Slide 72
luminosity - past&planned e+e- colliders
S. Henderson
TLEP-Z
TLEP-W
TLEP-H
TLEP-t
the circular route

## Slide 73
1. radiative Bhabha scattering (s≈0.215 barn)
LEP2: tbeam,LEP2~ 6 h
TLEP with L~5x1034 cm−2s−1 at 4 IPs:
tbeam,TLEP~21 minutes, unavoidable
2. beamstrahlung (synchr. rad. during the collision)
mitigated by:
(1) large momentum acceptance h
(2) flat beams [i.e. small ey & large bx*]
(3) fast replenishing
(M. Koratzinos, V.Telnov, K. Yokoya, M. Zanetti,…)
TLEP beam lifetime: two limits

## Slide 74
TLEP - circular e+e- collider to study
the «Higgs boson» X(126)
a relatively young concept (2011)
A. Blondel
short beam lifetime (~tLEP2/40) due to high luminosity
supported by top-up injection (used at KEKB, PEP-II, SLS,…)

## Slide 75: top-up injection: schematic cycle
10 s
energy of accelerator ring
120 GeV
20 GeV
injection into collider
injection into
accelerator
beam current in collider (15 min. beam lifetime)
100%
99%
almost constant current
acceleration time = 1.6 s
(assuming SPS ramp rate)

## Slide 76
K. Oide

## Slide 77: top-up performance at PEP-II/BaBar
Before Top-Up
After Top-Up
J. Seeman
average luminosity ≈ peak luminosity
J. Seeman

## Slide 78: proposed circular e+e- Higgs factories
FNAL site filler, 16 km
FNAL Snowmass proposal:
100 km “TLEP”
& FNAL VLLC 233 km ring
Chinese Higgs Factory CEPC
+ Super pp Collider
50 or 70 km
SuperTRISTAN in Tsukuba: 40 (& 60 or 80 “TLEP”) km
LEP3: 27 km
TLEP (LEP4): 80 km
near Geneva
SLAC/LBNL
design:
27 km
TLEP: 80 or 100 km
near Geneva
or HF in 27-km
LHC tunnel
(“LEP3”)
Qing QIN et al
Mike Koratzinos et al

## Slide 79
parameters | TLEP Z | TLEP W | TLEP H | TLEP t | 
Ec.m. [GeV] | 91 | 160 | 240 | 350 | 
beam current [mA] | 1440 | 154 | 29.8 | 6.7 | 
# bunches/beam | 7500 | 3200 | 167 | 160 | 20
#e−/bunch [1011] | 4.0 | 1.0 | 3.7 | 0.88 | 7.0
ex, ey [nm] | 29.2, 0.06 | 3.3,0.017 | 7.5, 0.015 | 2, .002 | 
β∗x,y [mm] | 500, 1 | 200, 1 | 500, 1 | 1000, 1 | 
σ∗x,y[μm] | 121, 0.25 | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13
σtotz,rms [mm] (w BS) | 2.93 | 1.98 | 2.11 | 0.77 | 1.95
ESRloss/turn [GeV] | 0.03 | 0.3 | 1.7 | 7.5 | 
VRF,tot [GV] | 2 | 2 | 6 | 12 | 
ξx,,y/IP | 0.068 | 0.086 | 0.094 | 0.057 | 
/IP[1034cm−2s−1] | 59 | 16 | 5 | 1.3 | 1.0
#IPs | 4 | 4 | 4 | 4 | 
tbeam[min] (rad.B) | 99 | 38 | 24 | 21 | 26
tbeam[min] (BS,h=2%) | >1025 | >106 | 38 | 14 | 2
parameters | TLEP Z | TLEP W | TLEP H | TLEP t | 
Ec.m. [GeV] | 91 | 160 | 240 | 350 | 
beam current [mA] | 1440 | 154 | 29.8 | 6.7 | 
# bunches/beam | 7500 | 3200 | 167 | 160 | 20
#e−/bunch [1011] | 4.0 | 1.0 | 3.7 | 0.88 | 7.0
ex, ey [nm] | 29.2, 0.06 | 3.3,0.017 | 7.5, 0.015 | 2, .002 | 
β∗x,y [mm] | 500, 1 | 200, 1 | 500, 1 | 1000, 1 | 
σ∗x,y[μm] | 121, 0.25 | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13
σtotz,rms [mm] (w BS) | 2.93 | 1.98 | 2.11 | 0.77 | 1.95
ESRloss/turn [GeV] | 0.03 | 0.3 | 1.7 | 7.5 | 
VRF,tot [GV] | 2 | 2 | 6 | 12 | 
ξx,,y/IP | 0.068 | 0.086 | 0.094 | 0.057 | 
 | 59 | 16 | 5 | 1.3 | 1.0
#IPs | 4 | 4 | 4 | 4 | 
tbeam[min] (rad.B) | 99 | 38 | 24 | 21 | 26
tbeam[min] (BS,h=2%) | >1025 | >106 | 38 | 14 | 2

## Slide 80
parameters | TLEP W | TLEP H | TLEP t |  | ZHH&ttH
Ec.m. [GeV] | 160 | 240 | 350 |  | 500
beam current [mA] | 154 | 29.8 | 6.7 |  | 1.6
# bunches/beam | 3200 | 167 | 160 | 20 | 10
#e−/bunch [1011] | 1.0 | 3.7 | 0.88 | 7.0 | 3.3
ex, ey [nm] | 3.3,0.017 | 7.5, 0.015 | 2, .002 |  | 4., 0.004
β∗x,y [mm] | 200, 1 | 500, 1 | 1000, 1 |  | 1000, 1
σ∗x,y[μm] | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13 | 63, 0.063
σtotz,rms [mm] (w BS) | 1.98 | 2.11 | 0.77 | 1.95 | 1.81
ESRloss/turn [GeV] | 0.3 | 1.7 | 7.5 |  | 31.4
VRF,tot [GV] | 2 | 6 | 12 |  | 35
ξx,,y/IP | 0.086 | 0.094 | 0.057 |  | 0.075
/IP[1034cm−2s−1] | 16 | 5 | 1.3 | 1.0 | 0.5
#IPs | 4 | 4 | 4 |  | 4
tbeam[min] (rad.B) | 38 | 24 | 21 | 26 | 13
tbeam[min] (BS,h=2%) | >106 | 38 | 14 | 2 | 3 (h=3%)
parameters | TLEP W | TLEP H | TLEP t |  | ZHH&ttH
Ec.m. [GeV] | 160 | 240 | 350 |  | 500
beam current [mA] | 154 | 29.8 | 6.7 |  | 1.6
# bunches/beam | 3200 | 167 | 160 | 20 | 10
#e−/bunch [1011] | 1.0 | 3.7 | 0.88 | 7.0 | 3.3
ex, ey [nm] | 3.3,0.017 | 7.5, 0.015 | 2, .002 |  | 4., 0.004
β∗x,y [mm] | 200, 1 | 500, 1 | 1000, 1 |  | 1000, 1
σ∗x,y[μm] | 26, 0.13 | 61, 0.12 | 45,.045 | 126,.13 | 63, 0.063
σtotz,rms [mm] (w BS) | 1.98 | 2.11 | 0.77 | 1.95 | 1.81
ESRloss/turn [GeV] | 0.3 | 1.7 | 7.5 |  | 31.4
VRF,tot [GV] | 2 | 6 | 12 |  | 35
ξx,,y/IP | 0.086 | 0.094 | 0.057 |  | 0.075
 | 16 | 5 | 1.3 | 1.0 | 0.5
#IPs | 4 | 4 | 4 |  | 4
tbeam[min] (rad.B) | 38 | 24 | 21 | 26 | 13
tbeam[min] (BS,h=2%) | >106 | 38 | 14 | 2 | 3 (h=3%)
TLEP
energy
upgrade

## Slide 81: optics – TLEP arc cell
r=3100 m, Lcell=79 m
r=9100 m, Lcell=50 m
Y. Cai,
B. Holzer,
H. Burkhardt
ex=48 nm at 104.5 GeV → ex=1.5 nm at 175 GeV
from LEP to TLEP
beta functions
dispersion
: at lower beam energy increase cell length (“q”) x2 or x6!

## Slide 82: SuperKEKB
beam commissioning will start in early 2015
by*=300 mm (TLEP: 1 mm)
lifetime 5 min (TLEP: ~15min)
ey/ex=0.25% ! (TLEP: 0.2%)
off momentum acceptance (±1.5%, TLEP: ±2%)
e+ production rate (2.5x1012/s, TLEP: <1x1011/s)
– a TLEP demonstrator

## Slide 83: other TLEP challenges
efficient RF system
  need 12 GeV/turn at 350 GeV
    ~600 m of SC RF cavities @ 20 MV/m
      LEP2 had 600 m at 7 MV/m
  very high power : up to 200 kW / cavity in collider ring
    power couplers similar to ESS –
    700-800 MHz preferred
operation at Z pole
  7500 bunches : e+ source, impedance effects, parasitic collisions
    two separate rings for e+ and e- beams will help here too
BNL 5-cell 700 MHz cavity
RF Coupler
(ESS/SPL)

## Slide 84: polarization
r = 9000 m, C = 80 km
U Wienands, April 2013
TLEP
optimized scenario
LEP
observations
+ model predictions
loss of polarization due to growing energy spread
 100 keV beam energy calibration by resonant depolarization (using pilot bunches) around Z peak and W pair threshold:
mZ ~0.1 MeV, Z ~0.1 MeV, mW ~ 0.5 MeV
A. Blondel
R. Assmann
lower energy spread, high polarization up to W threshold
LEP
TLEP
polarization scaling (energy spread!):
LEP at 61 GeV → TLEP at 81 GeV

## Slide 85: e+e- Higgs factories: luminosity
ultimate precision
at Z, WW, ZH ;
sensitive to New
Physics in multi-TeV range & to SM closure → case for VHE-LHC
ultimate energy reach
up to 1 or 3 TeV ;
direct searches
for New Physics

## Slide 86: vertical rms IP spot sizes in nm
LEP2 | 3500
KEKB | 940
SLC | 500
TLEP-H | 120
ATF2, FFTB | 60 (35), 60 (40)
SuperKEKB | 50
ILC | 5 – 8
CLIC | 1 – 2
in regular
font:
achieved
in italics:
design
values
TLEP
will learn
from ATF2 &
SuperKEKB
by*:
5 cm→
1 mm

## Slide 87: Higgs factory performances
Precision on couplings, cross sections, mass, width, Summary of the ICFA HF2012 workshop (FNAL, Nov. 2012) arxiv1302:3318
Circular Higgs Factory really goes to
precision at few per mill level

## Slide 88
CERN Courier article, 19 July 2013
John Ellis

## Slide 89
TLEP design study: http://cern.ch/tlep
where you can subscribe for work, information, newsletter , etc…
Global endeavour: collaborators from Europe, US, Japan, China, Mexico (!), …
Next events: 6th TLEP workshop 16-18 October, CERN
Joint VHE-LHC+ TLEP+VHE-LHeC kick-off meeting in February 2014
R. Aleksan,
A. Blondel,
J. Ellis,
P. Janot,
M. Koratzinos,
et al
welcome on board!

## Slide 90
VHE-LHC + TLEP
L. Rossi
multipurpose
tunnel
HE-LHC
(20 T)
HE-LHC-LER (0.17→1.5 T)
TLEP collider (0.07 or 0.05T)
TLEP injector (0.007→0.05/7 T)
20 mm thick shield around cable
Gaps: 2 x V30xH60 mm
transmission line magnet
(B. Foster, H. Piekarz)
super-resistive cable
based on MgB2 SC
only 12 MEuro/100 km!

## Slide 91: GMS-2T (TLEP)
GMS-4T (VHE-LHC)
common modular detectors for e+e- and pp collisions!?
E. Meschi

## Slide 92
PSB
PS (0.6 km)
SPS (6.9 km)
HL-LHC
TLEP (80-100 km,
e+e-, up to
~350 GeV c.m.)
VHE-LHC
(pp, up to
100 TeV c.m.)
possible long-term strategy
& e± (120 GeV) – p (7, 16 & 50 TeV) collisions ([(V)HE-]TLHeC)
≥50 years of e+e-, pp, ep/A physics at highest energies
CERN implementation
LHeC & SAPPHiRE?
LHC (26.7 km)

## Slide 93: conclusions – LHC & HL-LHC
LHC running well & predictably; LS1 in progress
in 2015 LHC will operate close to design energy with peak luminosity likely to exceed the design
new performance limits will be encountered (e.g. triplet cooling limit)
baseline for 2015 is 25 ns, but uncertainties: e-cloud & UFOs; backup option: 50 ns w leveling
HL-LHC well defined, prototype tests successful
plan & goals for HL-LHC under review
- budget considerations & LHC results

## Slide 94: conclusions – beyond HL-LHC
HL-LHC develops the technology (Nb3Sn magnets, 20-kA HTS cables) for future higher energy pp colliders: HE-LHC (33 TeV c.m.) and/or VHE-LHC (100 TeV c.m.)
TLEP, in VHE-LHC tunnel, being studied as highest-luminosity e+e- Higgs factory
- excellent energy resolution, & superb performance at Z pole , W & top threshold
coherent long-term strategy emerging, based on sharing, staging & synergies (high performance, minimum total cost, maximum energy reach)

## Slide 95
1980
1990
2000
2010
2020
2030
LHC
Constr.
Physics
Proto.
Design,
R&D
HL-LHC
Constr.
Physics
Design,
R&D
VHE-LHC
Constr.
Design,
R&D
2040
or TLEP
Constr.
Physics
Design,
R&D
Physics
HE-LHC
Constr.
Physics
Design,
R&D
{
?
LHeC/SAPPHiRE?
Constr.
Physics
Design,
R&D
possible long-term time line

## Slide 96
muchas gracias
dyos bo’otik

## Slide 97: spare slides

## Slide 98: Pb-Pb
good performance from the injectors - bunch intensity and emittance
preparation, Lorentz’ law: impressively quick switch from protons to ions
peak luminosity around 5 x 1026 cm-2s-1 at 3.5Z TeV (2011) – nearly twice design when scaled to 6.5Z TeV
M. Lamont, IPAC’13

## Slide 99: proton-lead
beautiful result in early 2013
final integrated luminosity above experiments’ request of 30 nb-1
injectors: average number of ions per bunch was ~1.4x108 at start of stable beams, i.e. around twice the nominal intensity
B1(p)
B2(Pb)
H(mm)
V(mm)
H(mm)
V(mm)
beam orbits at top energy with RF frequencies locked to Beam 1
M. Lamont, IPAC’13

## Slide 100
Shunts
still ahead of schedule but
the rate is not YET nominal
Weld M
late due to non availability of ICs to weld because of interference between insulation system and cryopipes
on the critical path
actual production rate good
SC Magnets and Circuits Consolidation
good overall progress : R2E ahead, SMACC on schedule (minor delays)
high number of splices to redo Baseline = 15%, Reality 25%-35%→addt’l resources
LS1 status (24 July 2013)
K. Foraz, LMC, 24 July 2013
>1/2 LHC opened, 15% shunts
installed and 3% M welds done

## Slide 101: HL-LHC optics
  Achromatic Telescopic Squeeze (ATS), «fully proven» MDs (* = 15 cm «easy», room for * ~ 10-12 cm)
typical ATS collision optics with IR1 & IR5 squeezed down to b*=10 cm
squeeze through
the arcs to enhance
effective sextupole
strength;
tested with beam
in LHC MDs of
2011 & 2012
S. Fartoukh

## Slide 102
L-R LHeC road map to ≥1033 cm-2s-1
luminosity of LR collider:
highest proton
beam brightness “permitted”
(ultimate LHC values)
ge=3.75 mm
Nb=1.7x1011
bunch spacing
25 or 50 ns
smallest conceivable
proton b* function:
reduced l* (23 m → 10 m)
squeeze only one p beam
new magnet technology Nb3Sn
b*p=0.1 m
maximize geometric
overlap factor
head-on collision
small e- emittance
qc=0
Hhg≥0.9
(round beams)
average e-
current
limited by
energy
recovery
efficiency
Ie=6.4 mA
HD~1.3
D. Schulte
LHeC2010

## Slide 103
synchroton-radiation: heat load
TLEP has >10 times less SR heat load per meter than PEP-II or SPEAR! (though higher photon energy)
N. Kurita, U. Wienands, SLAC

## Slide 104
A. Fasso
3rd TLEP3 Day
synchrotron radiation: activation
LEP design:
(r~3100 m)
higher photon energies
than TLEP!
(175 GeV,
r=9.1 or 11 km)

## Slide 105
TLEP cost breakdown – extremely rough (GEuro)
 | TLEP
Bare tunnel (with shafts & 8 caverns) | 3.1 (1)
Services & additional infrastructure (electricity, cooling, ventilation, service cavern, RP, surface structure, access roads) | 1.0 (2)
RF system | 0.7 (3)
Cryo system | 0.2 (4)
Vacuum system & RP | 0.5(5)
Magnet system for collider & injector ring | 0.8(6)
Pre-injector complex SPS reinforcements | 0.5
Total | 6.8
(1): J. Osborne, Amrup study
(2): very rough guess, conservative escalated extrapolation from LEP
(3): O. Brunner, Note, May 2013; B. Rimmer, SRF cost /GeV/Watt for CEBAF upgrade, 2010
(4): 2x LHeC cryo plant cost [Friedrich Haug, 4th TLEP workshop]
(5): factor 2.5 higher than KEK estimate for 80 km ring
(6): 24,000 magnets for collider & injector; cost per magnet 30 kCHF (LHeC study); 10% added; no cost saving from mass production assumed
Note: detector costs not included
preliminary – not endorsed by anybody

## Slide 106: Performance Comparison
J. Ellis et al.
Need sub-percent precision for sensitivity to multi-TeV New Physics
  Compare (LHC), HL-LHC, ILC, TLEP
    TLEP reaches the needed sub-percent accuracy
    much theoretical work also needed
HF2012
P. Janot
see talk by A. Blondel

## Slide 107: TLEP TeraZ, Oku-W & Mega-Top
Precision tests of EWSB
  measure mZ, GZ to < 0.1 MeV, mW to < 1 MeV, sin2θW to 2.10-6 from ALR
  TLEP beam polarization up to W threshold, for energy calibration
 | LEP | ILC | TLEP
√s ~ mZ | Mega-Z | Giga-Z | Tera-Z
#Z / year Polarization Precision vs LEP1 Error on mZ, GZ | 2×107 Yes (T) 1 2 MeV | Few 109 Easy 1/5 to 1/10 – | 1012 (>1011 b,c,t) Yes (T,L) ~1/100 < 0.1 MeV
√s ~ 2mW |  |  | 
#W pairs / year Polarization Error on mW | Few dozens No 220 MeV | 2×105 Easy 7 MeV | 2.5×107 Yes (T) 0.5 MeV
√s = 240 GeV |  |  | Oku-W
# W pairs / 5 years Error on mW | 4×104 33 MeV | 4×106 3 MeV | 2×108 0.5 MeV
√s ~ 350 GeV |  |  | Mega-Top
# top pairs / 5 years Error on mtop Error on lt | – – – | 100,000 30 MeV 40% | 500,000 13 MeV 15%
Asymmetries, Lineshape
WW threshold scan
WW production
tt threshold scan
TLEP : Repeat the LEP1 physics programme every 15 min
Transverse polarization up to the WW threshold
  Exquisite beam energy determination (10 keV)\
Longitudinal polarization at the Z pole
        Measure sin2θW to 2.10-6 from ALR
-
P. Janot
see talk by A. Blondel

## Slide 108
interim
F. Zimmermann ad interim
P. Janot ad interim
J. Ellis ad interim
R. Aleksan, A. Blondel, J. Ellis, P. Janot, M. Koratzinos, M. Zanetti, F. Zimmermann ad interim

## Slide 109: TLEP average power consumption rough estimate
system | el. power [MW]
RF (w/o cryogenics) | 180
RF for accelerator ring | 5
cryogenics | 34
cooling | 5
ventilation | 21
magnet systems | 14
general services | 20
total | ~274
large part of power (~200 MW) is proportional to beam current & luminosity; e.g. running
TLEP-H with 5x1034 cm-2s-1 (4 IPs) instead of 2x1035 cm-2s-1 total power would be ~120 MW
→ talks by
Mike Koratzinos
and Qing Qin

## Slide 110
beamstrahlung: lifetime & L spectrum
t>20 s at h=1.0%
t>3 min at h=1.5%
t>20 min at h=2.0%
t>4h at h=3%
simulation w 360M macroparticles (Guinea-Pig code)
 varies exponentially with momentum acceptance 
TLEP at 240 GeV: post-collision
E tail → beam lifetime 
beamstrahlung in circular collider much weaker than for LC
M. Zanetti (MIT)
luminosity energy
spectrum
required acceptance smaller for flatter beams

## Slide 111: beamstrahlung: equilibrium sz
beamstrahlung excites (surviving) e± longitudinally,
adding to effect of SR quantum excitation
→ collisions increase sz & sd (K. Yokoya)
1st ever self-consistent beam-beam simulations with BS (K. Ohmi):
weak strong
self-consistent
no beamstrahlung
2012 design
self-consistent
no BS
final bunch length from simulation
consistent w analytical expectation
including BS: sz=4.3 mm! (2012 TLEP parameters)
nonlinear
equation
bunch luminosity
rms bunch length

## Slide 112: luminosity with beamstrahlung
TLEP-H simulations for latest parameters
July 2013 parameters
May 2013 parameters
July 2013
May 2013
design luminosity
total luminosity / IP
rms bunch length
K. Ohmi, 17 July 2013
final bunch length from simulation
consistent w analytical expectation
including BS: sz=2.1 mm! (July 2013 parameters)

## Slide 113
FNAL site filler
±1.6%
IR optics - momentum acceptance h
±2.0%
SLAC/LBNL design
K. Oide
KEK design
after optics
correction
±1.3%
with synchrotron motion &
radiation
(sawtooth)
KEK design
before optics
correction
±1.1%
T. Sen, E. Gianfelice-Wendt, Y. Alexahin
Y. Cai

## Slide 114: optics - energy sawtooth
240 GeV, 40 km, 8 segments
350 GeV, 80 km, 16 segments
optics correction by shifting sextupoles onto sawtooth orbit
→ separate arcs/rings for e+ and e-
SuperTRISTAN
K. Oide

## Slide 115
collider parameters | TLHeC |  | VHE-TLHeC | 
species | e± | p | e± | p
beam energy [GeV] | 120 | 7000 | 120 | 50000
bunch spacing [ms] | 3 | 3 | 3 | 3
bunch intensity [1011] | 5 | 3.5 | 5 | 3.5
beam current [mA] | 24.3 | 51.0 | 24.3 | 51.0
rms bunch length [cm] | 0.17 | 4 | 0.17 | 2
rms emittance [nm] | 10,2 | 0.40 | 10,2 | 0.06
bx,y*[cm] | 2,1 | 60,5 | 0.5,0.25 | 60,5
sx,y* [mm] | 15, 4 |  | 6, 2 | 
beam-beam parameter x | 0.05, 0.09 | 0.03,0.01 | 0.07,0.10 | 0.03,0.007
hourglass reduction | 0.63 |  | 0.42 | 
CM energy [TeV] | 1.8 |  | 4.9 | 
luminosity [1034cm-2s-1] | 0.5 |  | 1.6 | 
parameters for TLHeC & VHE-TLHeC (e- at 120 GeV)

## Slide 116
collider parameters | TLHeC |  | VHE-TLHeC | 
species | e± | p | e± | p
beam energy [GeV] | 60 | 7000 | 60 | 50000
bunch spacing [ms] | 0.2 | 0.2 | 0.2 | 0.2
bunch intensity [1011] | 5 | 3.5 | 5 | 3.5
beam current [mA] | 390 | 51.0 | 390 | 51.0
rms bunch length [cm] | 0.18 | 4 | 0.18 | 2
rms emittance [nm] | 10, 2 | 0.40 | 10, 2 | 0.06
bx,y*[cm] | 2, 1 | 60, 5 | 0.5, 0.25 | 60,5
sx,y* [mm] | 15, 4 |  | 6, 2 | 
beam-beam parameter x | 0.10, 0.18 | 0.03,0.01 | 0.14, 0.20 | 0.03,0.007
hourglass reduction | 0.63 |  | 0.42 | 
CM energy [TeV] | 1.3 |  | 3.5 | 
luminosity [1034cm-2s-1] | 8.0 |  | 25.6 | 
parameters for TLHeC & VHE-TLHeC (e- at 60 GeV)

## Slide 117: How a Particle Accelerator Works
-
-
-
-
Old-style television: Cathode ray tube
Anode (+)
Anode (+)
Filament
Cathode (-)
Electron beam
Focussing system
Steering system
Fluorescent screen

## Slide 118: A Circular ‘Synchrotron’ Accelerator
+
-
The magnetic field is increased to keep the particles circulating with the same circumference as the energy increases