## Slide 1
Future Highest-Energy Circular Colliders
F. Zimmermann, CERN BE/ABP
Physics Colloquium, Johannes Gutenberg U.
Mainz, 6 January 2015
Work supported by the European Commission under Capacities 7th Framework Programme, Grant Agreement 312453
gratefully acknowledging input from FCC global design study & CepC/SppC team

## Slide 2
Large Hadron Collider (LHC)
c.m. energy
14 TeV (pp)
luminosity
1034 cm-2s-1
1.15x1011 p/bunch
2808 bunches/beam
360 MJ / beam
dipole field 8.33 T

## Slide 3
luminosity
reaction rate
luminosity
R= s L
C. Amsler et al., Physics Letters B667, 1 (2008)
from
cosmic rays
LHC
cross section
tot~
100 mbarn
~ 10-25 cm2
inelastic~
75 mbarn~
7.5x10-26cm2
sHiggs ~ 30 pb → with 300 fb-1 LHC produces ~ 10 million Higgs
TOTEM, EPL 101 (2013) 21004

## Slide 4: Luminosity
N | Number of particles per bunch
kb | Number of bunches
f | Revolution frequency
σ* | Beam size at interaction point
F | Reduction factor due to crossing angle
ε | Emittance
εn | Normalized emittance
β* | Beta function at IP
Round beams, beam 1 = beam 2
M. Lamont

## Slide 5
1 SPS batch
(144 bunches)
26.7 km - 1380 bunches in 2012, ~2800 in 2015
1 PS batch
(36 bunches)
John Jowett
betamax ~4.5 km
beta* 60 cm
Abort gap
M. Lamont
25 ns (7.5 m)

## Slide 6: LHC Integrated luminosity 2010-2012
2010: 0.04 fb-1
  7 TeV CoM
  Commissioning
2011: 6.1 fb-1
  7 TeV CoM
  Exploring the limits
2012: 23.3 fb-1
  8 TeV CoM
  Production

## Slide 7: LHC peak performance through the years
 | 2010 | 2011 | 2012 | Nominal
Bunch spacing [ns] | 150 | 50 | 50 | 25
No. of bunches | 368 | 1380 | 1380 | 2808
beta* [m] ATLAS and CMS | 3.5 | 1.0 | 0.6 | 0.55
Max bunch intensity [protons/bunch] | 1.2 x 1011 | 1.45 x 1011 | 1.7 x 1011 | 1.15 x 1011
Normalized emittance [mm.mrad] | ~2.0 | ~2.4 | ~2.5 | 3.75
Peak luminosity [cm-2s-1] | 2.1 x 1032 | 3.7 x 1033 | 7.7 x 1033 | 1.0 x 1034
M. Lamont

## Slide 8
8
Huge efforts over last months to prepare for high lumi and pile-up expected in 2012:
optimized trigger and offline algorithms (tracking, calo noise treatment, physics objects)
 mitigate impact of pile-up on CPU, rates, efficiency, identification, resolution
in spite of x2 larger CPU/event and event size  we do not request additional computing
resources (optimized computing model, increased fraction of fast simulation, etc.)
Z μμ
Z μμ event from 2012 data with 25 reconstructed vertices
pile up
will increase
at higher energy
→
experiments
request
25 ns
operation
in 2015
M. Lamont, IPAC’13

## Slide 9: LHCb
luminosity levelling at around 4e32 cm-2s-1 via transverse separation
(with tilted crossing angle)
ATLAS/CMS
LHCb
first evidence for the decay Bs -> m+ m-
M. Lamont, IPAC’13

## Slide 10
M. Lamont
LHC injector complex

## Slide 11
Week 2: last interventions (excl. collimator exchange and ELQA) and patrols
Week 10: last quench training in parallel with cold check-out ?
K. Foraz
LHC restart schedule (as of 17 Dec. 2014)

## Slide 12
training quenches in the LHC
& first training quench in SM18
Chart: 
Training quench | 10004 | 10227 | 10358 | 10545 | 10652 | 10714 | 10751 | 10793 | 10834 | 10882 | 10910 | 10720 | 10918 | 10944 | 10976 | 10976 | 10986 | 10997 | 11019 | 11040 | 11067 | 11075 | 11090
Training Quench in 67
Training Quench in 12
HWC target for 6.5TeV | 11080 | 11080
Chart: 
Training quench | 9779 | 9951 | 10035 | 10126 | 10006 | 10352 | 10469 | 10509 | 10536 | 10641 | 10644 | 10703 | 10728 | 10750 | 10856 | 10961 | 10970 | 11009 | 11041 | 11053
Training Quench in 56
Training Quench in 12
HWC target for 6.5TeV | 11080 | 11080
Sector 12
Sector 56 in 2008
Sector 67
2 Firm1
1 Firm 2
«2» Firm 3
0 Firm 1
2 Firm 2
19 Firm 3
0 Firm 1
1 Firm 2
19 Firm 3
Chart: Current [A]
Training quench | 9380 | 10157 | 10363 | 10533 | 10755
Training Quench in 67
Training Quench in 12
HWC target for 6.5TeV | 11080 | 11080
S. Le Naour

## Slide 13: LHC - 2015
Target energy: 6.5 TeV
  to be confirmed at end of powering tests
Bunch spacing: 25 ns
  strongly favored by experiments (pile-up limit ~ 50)
Beta*: 80 to 40 cm
  Lower quench margins
  Lower tolerance to beam loss
  Lower intensity set-up beams
  Hardware closer to maximum (beam dumps, power converters etc.)
Energy
  E-cloud, UFOs
  More long range collisions
  Larger crossing angle, higher beta*
  Higher total beam current
  Higher intensity per injection
25 ns
M. Lamont

## Slide 14
 | Nc | beta* [cm] | ppb | EmitN [um] | Lumi [cm-2s-1] | Days (approx) | Int lumi | Pileup
50 ns | 1300 | 80 | 1.2e11 | 2.5 | 4.6e33 | 21 | ~1 fb-1 | 27
25 ns (1) | 2496 | 80 | 1.1e11 | 2.5 | 7.4e33 | 75 | 6.8 fb-1 | 22
25 ns (2) | 2496 | 40 | 1.1e11 | 2.5 | 1.3e34 | 46 | 9.2 fb-1 | 39
Start with 50 ns – scrub – 25 ns operation
Conservative beta* to start
Conservative bunch population
Reasonable emittance into collisions
Assuming same machine availability as 2012…
Will lay the foundations for Run 2…
M. Lamont
2015 - potential performance

## Slide 15: 10 year plan
Run 3: 14 TeV c.m. with peak luminosity of ~2x1034 cm-2 s-1
Run 2: 13 to 14 TeV c.m. with peak luminosity of ~1.7x1034 cm-2 s-1
Long years – 13 weeks Christmas stop
Interspersed with long shutdown every 3 to 4 years
Ions very much part of the plan
LS2: 18 months
Connection of LINAC4
LHC Injectors Upgrade
EYETS ~5 months
Extended year end technical stop (CMS)
LS3: 30 months
High Luminosity LHC
M. Lamont

## Slide 16
With the discovery of a Higgs boson in 2012, we have completed the Standard Model (almost 80 years of theoretical and experimental efforts !)
However: SM is not a complete theory
Several outstanding questions (e.g. composition of dark matter, cause of universe’s accelerated expansion [dark energy / inflation], origin of matter-antimatter asymmetry, neutrino masses, why 3 families?, lightness of Higgs boson, weakness of gravity, … ) which cannot be explained within the SM.
These questions require NEW PHYSICS
Prospects for Particle Physics
Present knowledge is insufficient to determine energy scale of new physics ; LHC will provide new information from pp collisions at higher cm energy (13 TeV) by 2017-18
F. Gianotti et al.

## Slide 17
main questions in particle physics and main approaches to address them
question | high-energy colliders | high-precision experiments | neutrino experiments | dedicated searches | cosmic surveys
Higgs, EWSB | X |  |  |  | 
neutrinos | X |  | X | X | X
dark matter | X |  |  | X | 
flavour, CP violation | X | X | X | X | 
new particles and forces | X | X | X | X | 
universe acceleration |  |  |  |  | X
most of these questions require high-energy and/or
high-intensity accelerators
F. Gianotti et al.

## Slide 18
Run 2
Run 3
Run 4
LS 2
LS 3
LS 4
LS 5
Run 5
LS2 starting in 2018 (July) => 18 months + 3 months BC
LS3 LHC: starting in 2023 => 30 months + 3 months BC
Injectors: in 2024 => 13 months + 3 months BC
LHC roadmap: schedule until 2035
Beam commissioning
Technical stop
Shutdown
Physics
Run 2
Run 3
Run 4
LS 2
LS 3
LS 4
LS 5
Run 5
(Extended) Year End Technical Stop: (E)YETS
EYETS
YETS
YETS
YETS
YETS
YETS
300 fb-1
3’000 fb-1
30 fb-1
PHASE 1
PHASE 2
F. Bordry
Phase 2: HL-LHC

## Slide 19
3000 fb-1 delivered in the order of 10 years
High “virtual” luminosity with levelling anticipated
Challenging demands on the injector complex
  major upgrades foreseen
5 x 1034 cm-2s-1
levelled luminosity
Pile-up ~140
3 fb-1 per day
~250 fb-1 /year
M. Lamont
HL-LHC

## Slide 20
technology transition: Nb-Ti →Nb3Sn
O. Bruning

## Slide 21
more than 1.2 km of LHC plus technical infrastructure (e.g. Cryo and Powering)
compact Crab Cavities
Nb3Sn dipoles & quadrupoles
ATLAS
New quadrupole triplet based on Nb3Sn (12 T at coil)
required due to:
-Radiation damage
-Need for more aperture
Changing the triplet region is not enough for reaching the HL-LHC goal!
2. We also need to modify a large part of the matching section
e.g. Crab Cavities &
D1, D2, Q4 & corrector
3. For collimation we also need to change the DS in the continuous cryostat: 11-T Nb3Sn dipole
CMS
O. Brüning,
L. Rossi
HL-LHC - critical zones around IP1 & IP5

## Slide 22
MBHSP02 (1 m) passed 11 T field during training at 1.9 K with I = 12080 A on 5 March 2013
FNAL: Nb3Sn 11-T dipole demonstrators
US-LARP

## Slide 23
FNAL Nb3Sn 1-m 11(12)-T dipole models
MBHSP02, MBHSP03
MBHSM01
MBHSP02:
  Bmax=11.7 T at 1.9 K
  97.5% of Bdes=12 T
MBHSP03:
  Bmax=11.7 T at 1.9 K
  97.5% of Bdes=12 T
MBHSM01:
    Bmax=12.5 T at 1.9 K
    ~100 (97)% at 4.5 (1.9) K of SSL
A. Zlobin
US-LARP

## Slide 24
CERN Nb3Sn 2-m 11-T dipole models
trained up to 97 % of Iss at 1.9 K
- good memory
coils 106 & 107: 4 & 19 training quenches up to nominal current
MBHSP101: single aperture
MBHSM101: single coil
also at CERN, in 2012 two pairs of racetrack coils obtained 12.5 T in the winding at 1.9 K
CERN
G. Willering

## Slide 25
1983 first LHC proposal, launch of design study
1994 CERN Council: LHC approval
2010 first collisions at 3.5 TeV beam energy
2015 collisions at design energy (plan)
now is the time to plan for 2040!
LHC history

## Slide 26
European Strategy Update 2013
“CERN should undertake design studies for accelerator projects in a global context, with emphasis on proton-proton and electron-positron high-energy frontier machines.”
strategy adopted by the CERN Council
http://cds.cern.ch/record/1567258/files/esc-e-106.pdf

## Slide 27
Future Circular Collider Study - SCOPE
CDR and cost review for the next ESU (2018)
Forming an international collaboration to study:
pp-collider (FCC-hh)  defining infrastructure requirements
80-100 km infrastructure in Geneva area
e+e- collider (FCC-ee) as potential intermediate step
p-e (FCC-he) option
~16 T  100 TeV pp in 100 km
~20 T  100 TeV pp in 80 km
www.cern.ch/fcc
M. Benedikt

## Slide 28
Qinhuangdao (秦皇岛）
50 km
70 km
easy access
300 km from Beijing
3 h by car
1 h by train
Yifang Wang
CepC, SppC
CepC/SppC study (CAS-IHEP), CepC CDR end of 2014, e+e- collisions ~2028; pp collisions ~2042
“Chinese Toscana”

## Slide 29
CepC/SppC project – recent news in Nature
24 J U LY 2014 | VO L 511 | NAT U R E | 3

## Slide 30
previous studies in Italy (ELOISATRON 300 km), US (SSC 87 km, VLHC/VLLC 233 km) & Japan (94 km)
ex. SSC
Supercolliders Superdetectors: Proceedings of the 19th and 25th Workshops of the INFN Eloisatron Project
ex. ELOISATRON
SSC CDR 1986
H. Ulrich Wienands, The SSC Low Energy Booster: Design and Component Prototypes for the First Injector Synchrotron,
IEEE Press 1997
VLHC Design Study Group Collaboration June 2001. 271 pp.
SLAC-R-591, SLAC-R-0591, SLAC-591, SLAC-0591, FERMILAB-TM-2149
http://www.vlhc.org/
ex. VLHC
ex. TRISTAN-II
study 1983

## Slide 31
Courtesy V. Shiltsev
pp
e+e-
factor 10 every
20-30 years
factor 10 every
10 years
factor 105-107 in e+e-
luminosity
collider c.m. energy vs. year
Ecm=2ec Br
hadron-lepton
FCC-he
LHeC
ep

## Slide 32
FCC-hh: 100 TeV pp collider
LHC
27 km, 8.33 T
14 TeV (c.m.)
FCC-hh (alternative)
80 km, 20 T
100 TeV (c.m.)
FCC-hh (baseline)
100 km, 16 T
100 TeV (c.m.)
“HE-LHC”
27 km, 20 T
33 TeV (c.m.)
Geneva
PS
SPS
LHC
L. Bottura
B. Strauss

## Slide 33
➥ Access to new particles in the few TeV to 30 TeV mass range, beyond LHC reach
➥ Immense/much-increased rates for
phenomena in the sub-TeV mass range →
increased precision w.r.t. LHC and possibly ILC
➥ Access to very rare processes in the sub-TeV mass range → search for stealth phenomena, invisible at the LHC
FCC-hh opens three physics windows
M. Mangano

## Slide 34
FCC-hh key parameters
parameter | FCC-hh | LHC
energy | 100 TeV c.m. | 14 TeV c.m.
dipole field | 16 T | 8.33 T
# IP | 2 main, +2 | 4
normalized emittance | 2.2 mm | 3.75 mm
luminosity/IPmain | 5 x 1034 cm-2s-1 | 1 x 1034 cm-2s-1
energy/beam | 8.4 GJ | 0.39 GJ
synchr. rad. | 28.4 W/m/apert. | 0.17 W/m/apert.
bunch spacing | 25 ns (5 ns) | 25 ns
Preliminary, subject to evolution (several luminosity scenarios)

## Slide 35
Cms energy |  |  | 
Luminosity |  |  | 
parameter | LHC | HL-LHC | FCC-hh
c.m. energy [TeV] | 14 |  | 100
dipole magnet field [T] | 8.33 |  | 16 (20)
circumference [km] | 26.7 |  | 100 (83)
luminosity [1034 cm-2s-1] | 1 | 5 | 5 [→20?]
bunch spacing [ns] | 25 |  | 25 {5}
events / bunch crossing | 27 | 135 | 170 {34}
bunch population [1011] | 1.15 | 2.2 | 1 {0.2}
norm. transverse emitt. [mm] | 3.75 | 2.5 | 2.2 {0.44}
IP beta-function [m] | 0.55 | 0.15 | 1.1
IP beam size [mm] | 16.7 | 7.1 | 6.8 {3}
synchrotron rad. [W/m/aperture] | 0.17 | 0.33 | 28 (44)
critical energy [keV] | 0.044 |  | 4.3 (5.5)
total syn.rad. power [MW] | 0.0072 | 0.0146 | 4.8 (5.8)
longitudinal damping time [h] | 12.9 |  | 0.54 (0.32)
FCC-hh baseline parameters defined in EDMS No. 1342402, FCC-ACC-SPC-0001

## Slide 36: ring optics for alternative layouts
R. Alemany,
B. Holzer,
R. Tomas,
D. Schulte
bx,y [m]
Dx [m]
LHC-like
circular
SSC-like
race-
track
C=99.13 km
C=100.8 km
Linsertion~7.4 km
work in progress
FODO arc
optics,
cell length
~200 m

## Slide 37: FCC topography
Plaine du genevois
350 – 550 m/mer
Mont Salève
550 - 1380
Lac Léman
300 – 372 m/mer
Plateau des Bornes
600 – 850 m/mer
Valée de l’Arve
400 – 600 m/mer
Mandallaz
Mont Vuache
550 - 1100
Massif du Jura
550 – 1720 m/mer
Bornes – Aravis
600 – 2500 m/mer
Plateau du Mont Sion
550 – 860 m/mer
Pré-Alpes du Chablais
600 – 2500 m/mer
Vallon des Usses
380 – 500 m/mer
Vallée du Rhône
330 m/mer
J. Osborne

## Slide 38: FCC tunnel configuration
Ph. Lebrun
38
FCC circumference is a multiple of LHC :
  80 km
  87 km
  93 km
  100 km

## Slide 39
only a quarter is shown
15-16 T: Nb-Ti & Nb3Sn
20 T: Nb-Ti & Nb3Sn & HTS
L. Rossi, E. Todesco, P. McIntyre
“hybrid magnets”
example block-coil layout
cost-optimized high-field dipole magnets

## Slide 40: From ITER- to HEP-class Nb3Sn
ITER
US-CDP
CARE-NED
EuCARD
HL-LHC
HL-LHC specs
FCC
FCC specs
L. Bottura

## Slide 41: machine protection
energy per proton beam
LHC: 0.4 GJ → FCC-hh: 8 GJ (20x more !)
  kinetic energy of Airbus A380 at 720 km/h
  can melt 12 tons of copper, or drill a 300-m long hole

## Slide 42: FCC-hh injector complex
B. Goddard,
W. Herr, et al.
based on existing & planned (HL-LHC/LIU) injector chain;
HEB in LHC tunnel (e.g. modified LHC) or FCC tunnel

## Slide 43
LEP – highest energy e+e- collider so far
maximum c.m. energy 209 GeV
maximum synchrotron radiation power 23 MW

## Slide 44: physics requirements for FCC-ee
highest possible luminosity for a wide physics program ranging from the Z pole to the production threshold
  beam energy range from 45 GeV to 175 GeV
main physics programs / energies:
  Z (45.5 GeV): Z pole, ‘TeraZ’ and high precision MZ & GZ,
  W (80 GeV): W pair production threshold,
  H (120 GeV): ZH production (maximum rate of H’s),
  t (175 GeV): threshold
some polarization up to ≥80 GeV for beam energy calibration
optimized for operation at 120 GeV?!

## Slide 45
FCC-ee key parameters
parameter | FCC-ee | LEP2
energy/beam | 45 – 175 GeV | 105 GeV
bunches/beam | 98 – 16700 | 4
beam current | 6.6 – 1450 mA | 3 mA
hor. emittance | ~2 nm | ~22 nm
emittance ratio ey/ey | 0.1% | 1%
vert. IP beta function by* | 1 mm | 50 mm
luminosity/IP | 1.8-28 x 1034 cm-2s-1 | 0.0012 x 1034 cm-2s-1
energy loss/turn | 0.03-7.55 GeV | 3.34 GeV
synchr. power | 100 MW | 23 MW
RF voltage | 2.5 – 11 GV | 3.5 GV
Preliminary, subject to evolution (staging scenarios)

## Slide 46
parameter | LEP2 | FCC-ee |  |  |  |  | CepC
 |  | Z | Z (c.w.) | W | H | t | H
Ebeam [GeV] | 104 | 45 | 45 | 80 | 120 | 175 | 120
circumference [km] | 26.7 | 100 | 100 | 100 | 100 | 100 | 54
current [mA] | 3.0 | 1450 | 1431 | 152 | 30 | 6.6 | 16.6
PSR,tot [MW] | 22 | 100 | 100 | 100 | 100 | 100 | 100
no. bunches | 4 | 16700 | 29791 | 4490 | 1360 | 98 | 50
Nb [1011] | 4.2 | 1.8 | 1.0 | 0.7 | 0.46 | 1.4 | 3.7
ex [nm] | 22 | 29 | 0.14 | 3.3 | 0.94 | 2 | 6.8
ey [pm] | 250 | 60 | 1 | 1 | 2 | 2 | 20
b*x [m] | 1.2 | 0.5 | 0.5 | 0.5 | 0.5 | 1.0 | 0.8
b*y [mm] | 50 | 1 | 1 | 1 | 1 | 1 | 1.2
s*y [nm] | 3500 | 250 | 32 | 130 | 44 | 45 | 160
sz,SR [mm] | 11.5 | 1.64 | 2.7 | 1.01 | 0.81 | 1.16 | 2.3
sz,tot [mm] (w beamstr.) | 11.5 | 2.56 | 5.9 | 1.49 | 1.17 | 1.49 | 2.7
hourglass factor Fhg | 0.99 | 0.64 | 0.94 | 0.79 | 0.80 | 0.73 | 0.61
L/IP [1034 cm-2s-1] | 0.01 | 28 | 212 | 12 | 6 | 1.7 | 1.8
tbeam [min] | 300 | 287 | 39 | 72 | 30 | 23 | 40
the large number of bunches at Z, W & H requires 2 rings
short lifetimes due to high luminosity → continuous injection (top-up)

## Slide 47: FCC-ee luminosity vs energy
Z
W
H
crab waist & improved parameters
baseline
M. Benedikt, A. Blondel, A. Bogomyagkov, E. Levichev, D. Shatilov, J. Wenninger, F. Zimmermann,…

## Slide 48: emittances in good company
Y. Papaphilippou

## Slide 49: FCC-ee injection
beside the collider ring(s), a booster of the same size (same tunnel) must provide beams for top-up injection
  same RF voltage, but low power (~ MW)
  top up frequency ~0.1 Hz
  booster injection energy ~5-20 GeV
  bypass around the experiments
injector complex for e+ and e- beams of 10-20 GeV
  Super-KEKB injector ~ almost suitable
A. Blondel

## Slide 50: SuperKEKB = FCC-ee demonstrator
beam commissioning will start in 2015
top up injection at high current
by* =300 mm (FCC-ee: 1 mm)
lifetime 5 min (FCC-ee: ≥20 min)
ey/ex =0.25% (similar to FCC-ee)
off momentum acceptance (±1.5%, similar to FCC-ee)
e+ production rate (2.5x1012/s, FCC-ee: <1.5x1012/s (Z cr.waist)
SuperKEKB goes beyond FCC-ee, testing all concepts
K. Oide et al.

## Slide 51: layout & optics at 120 & 175 GeV
S
B
Q
B = bending magnet, Q = quadrupole, S = sextupole
Q
B
BPM
Corrector
B
B
S
Q
arc cell
Lattice V12b-s
Circumference: 100 km
Arc length: 2 × 3.4 km
Straight section: 1.5 km
layout
B. Harer, B. Holzer
0
20
40
60
80
100
0
2
4
6
8
10
12
b
e
t
x
i
n
m
s in km
FODO cell optics
cell length 50 m
full ring optics

## Slide 52: optics 175 & 120 → 80 & 45.5 GeV
example: 100 m cell length
example: 300 m cell length
80 GeV
45.5 GeV
B. Harer, B. Holzer
all emittances ex ≤ 0.5 baseline

## Slide 53: synchrotron radiation power
The maximum synchrotron radiation (SR) power PSR is set to 50 MW per beam – design choice  power dissipation.
  defines the maximum beam current at each energy.
  Note that a margin of a few % is required for losses in straight sections.
  r = 11 km
  r = 3.1 km
VRF ~10-11 GV
VRF ~35 GV
J.Wenninger

## Slide 54: SC RF System
RF system requirements are characterized by two regimes.
  High gradients for H and – up to ~11 GV.
  High beam loading with currents of ~1.5 A at the Z pole.
RF system must be distributed over the ring to minimize energy excursions (~4.5% energy loss @ 175 GeV).
  Optics errors driven by energy offsets, effect on h.
Aiming for SC RF cavities with gradients of ~20 MV/m.
RF frequency of 400 & 800 MHz (current baseline).
  Nano-beam / crab waist favors lower frequency, e.g. 400 MHz.
Conversion efficiency (wall plug to RF power) is critical. Aiming for 75% or higher  R&D !
  An important item for FCC-ee power budget.~65% achieved for LEP2.
J. Wenninger, A. Butterworth, E. Jensen, et al.

## Slide 55: luminosity
H  1
Hour-glass
2F
F  1
Crossing angle
Beam-beam parameter
J. Wenninger

## Slide 56: beam-beam parameter
beam-beam parameter x measures strength of field sensed by the particles in a collision
beam-beam parameter limits are empirically scaled from LEP data (also 4 IPs)
In reasonable agreement with first simulations for FCC ee
The beam-beam limit may be raised significantly with Crab-Waist schemes !
J. Wenninger, R. Assmann, S. White, K. Ohmi, D. Shatilov, et al.
R. Assmann & K. Cornelis, EPAC2000

## Slide 57: beamstrahlung
hard photon emission at the IPs, ‘Beamstrahlung’, can become lifetime / performance limit for large bunch populations (N), small hor. beam size (sx) & short bunches (ss)
r : mean bending radius at the IP (in the field of the opposing bunch)
to ensure an acceptable lifetime, rh must be sufficiently large
  flat beams (large sx) !
  bunch length !
  large momentum acceptance of the lattice: 1.5 – 2% required.
    LEP: < 1% acceptance, SuperKEKB ~ 1-1.5%.
h : ring energy acceptance
g
e
e
lifetime expression by V. Telnov, modified version by A. Bogomyagkov et al
J. Wenninger, et al

## Slide 58: beam-beam limits: 2 regimes
Chart: beam energy (GeV)
| 100 | 110 | 120 | 130 | 140 | 150 | 160 | 175 | 180 | 190 | 200
beam-beam limit | 0.072102 | 0.080838 | 0.089735 | 0.098782 | 0.10797 | 0.11729 | 0.12673 | 0.14112 | 0.14597 | 0.15576 | 0.16565
vertical emittance 2pm, momentum acceptance 2% | 0.22589 | 0.22589 | 0.14393 | 0.14393 | 0.11174 | 0.11174 | 0.10395 | 0.10395 | 0.083959
vertical emittance 2pm, momentum acceptance 1.5% | 0.1969 | 0.1969 | 0.11894 | 0.11894 | 0.085458 | 0.085458 | 0.071965 | 0.071965 | 0.068366 | 0.068366 | 0.058671
beamstrahlung
lifetime w. h=1.5%
beamstrahlung
lifetime (300 s) w. h=2.0%
ey = 2 pm,
by* = 1 mm
M. Koratzinos, A. Bogomyagkov, E. Levichev, D. Shatilov, K. Yokoya, V. Telnov, K. Oide, …

## Slide 59
Precision Measurements
Springboard for sensitivity to new physics
Theoretical issues:
  Higher-order QCD
  Higher-order EW
  Mixed QCD + EW
Rare Decays
Direct searches for new physics
Many opportunities
Z: 1012
b, c, τ: 1011
W: 108
H: 106
t: 106
The Twin Frontiers of FCC-ee Physics
J. Ellis
P. Janot
M. Ruan
M. Bicer et al., “First Look at the Physics Case of TLEP,’’ JHEP 01, 164 (2014)
S. Dawson et al., arXiv:1310.8361v2
Higgs coupling
measurements
HL-LHC
ILC500
FCC-ee 350
CepC, 4/ab

## Slide 60: high-energy lepton-hadron collider
RR LHeC:
new ring
in LHC tunnel,
with bypasses
around
experiments
LR LHeC:
recirculating
linac with
energy
recovery
similar two options for FCC:
(1) FCC-ee ring, (2) ERL – from LHeC or new
LHeC CDR , published in 2012

## Slide 61
h-e Higgs-boson production and decay; and precision measurements of the H–bb coupling in WW–H production; FCC-he also gives access to Higgs self-coupling H–HH (<10% precision!? - under study), to lepto-quarks up to ≈4 TeV & to Bjorken x as low as 10-7 - 10-8 [of interest for ultra high energy n scattering]
Higgs physics at LHeC & FCC-he
M. Klein and H. Schopper, CERN Courier June2014

## Slide 62
 | HL-LHC | LHeC | ILC | CLIC | FCC-ee/hh | CepC/SppC
leptons | - | cw SRF at 800 or 400 MHz | Pulsed SRF at 31.5 MV/m at 1.3 GHz | Pulsed NC RF at 100 MV/m at 12 GHz | cw SRF at 800 or 400 MHz with 15-20 MV/m | cw SRF at 650 MHz with 15.5 MV/m (& 1.3 GHz booster)
 | - | RF power source | RF power source | RF power source | RF power source | RF power source
 | - | High-E high-I ERL | final focus | final focus | IR optics with large E acceptance | IR optics with large E acceptance
 | - |  | damping ring | drive beam dynamics |  | Pretzel scheme
 | - |  | e+ source | e+ source |  | 
hadrons | 11-12 T Nb3Sn dipoles & quad’s | - | - | - | 15-16 T Nb3Sn dipoles & quad’s | 19-20 T HTS dipoles
 | Compact crab cavities | - | - | - | efficient cooling of SR | efficient cooling of SR
 | SC link | - | - | - |  | 
collider technology “readiness matrix”
color code:
state of the art
not fully demonstrated
more R&D needed

## Slide 63
2014 |  |  |  | 2015 |  |  |  | 2016 |  |  |  | 2017 |  |  |  | 2018 |  |  | 
Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4 | Q1 | Q2 | Q3 | Q4
Kick-off, collaboration forming,
study plan and organisation
Release CDR & Workshop on next steps
Workshop & Review
 contents of CDR
Workshop & Review identification of baseline
Ph 2: Conceptual study of baseline “strong interact.”
Workshop & Review, cost model, LHC results  study re-scoping?
Ph 3: Study
consolidation
Report
Prepare
4 large FCC Workshops distributed over participating regions
Ph 1: Explore options
“weak interaction”
FCC global design study – time line
M. Benedikt
we are here

## Slide 64
http://indico.cern.ch/e/fcc-kickoff
http://cern.ch/fcc
FCC Kick-off Meeting
University of Geneva
12-15 February 2014
>340 participants

## Slide 65
presently signing FCC MoUs with partners

## Slide 66
FCC MoU’s, status 9 Dec. 2014
ALBA/CELLS, Spain
U. Bern, Switzerland
BINP, Russia
CASE (SUNY/BNL), USA
CBPF, Brazil
CEA Grenoble, France
CIEMAT, Spain
CNRS, France
Cockcroft Institute, UK
U Colima, Mexico
CSIC/IFIC, Spain
TU Darmstadt, Germany
DESY, Germany
TU Dresden, Germany
Duke U., USA
EPFL, Switzerland
Gangneung-Wonju Nat. U., Korea
U Geneva, Switzerland
Goethe U. Frankfurt, Germany
GSI, Germany
Hellenic Open U, Greece
HEPHY, Austria
IFJ PAN Krakow, Poland
INFN, Italy
INP Minsk, Belarus
U Iowa, USA
IPM, Iran
Istanbul Aydin U. ,Turkey
JAI/Oxford, UK
JINR Dubna, Russia
KEK, Japan
KIAS, Korea
King’s College London, UK
Korea U. Sejong, Korea
MEPhI, Russia
Northern Illinois U., USA
NC PHEP Minsk, Belarus
PSI, Switzerland
Sapienza/Roma, Italy
UC Santa Barbara, USA
U Silesia, Poland
TU Tampere, Finland

## Slide 67
Study Coordination
Hadron Collider Physics and Experiments
Lepton Collider Physics and Experiments
Hadron Injectors
Hadron Collider
Lepton Collider
e-p Physics, Experiments, IP Integration
Infrastructures and Operation
Lepton Injectors
Accelerator R & D Technologies
F. Gianotti, A. Ball, M. Mangano
A. Blondel, J. Ellis, C. Grojean, P. Janot
M. Klein, O. Bruning
B. Goddard
D. Schulte, M. Syphers, J.M. Jimenez
Y. Papaphilippou
J. Wenninger, U. Wienands, J.M. Jimenez
M. Benedikt, F. Zimmermann
P. Lebrun, P. Collier
F. Sonnemann, P. Lebrun
FCC Study Coordination Group
Costing Planning
M. Benedikt, F. Zimmermann

## Slide 68
FCC Collaboration Board
preparatory meeting 9-10 September 2014 at CERN (~80 participants, 1 / inst.)
Leonid “Lenny” Rivkin (EPFL & PSI) unanimously elected as interim Collaboration Board Chair

## Slide 69
FCC Horizon 2020 Design Study Proposal
submitted to Brussels on
2 September 2014
key aspects of 100 TeV energy frontier hadron collider:
conceptual design, feasibility, implementation scenario

## Slide 70
Physics and Experiments
Accelerators
Infrastructures and Operation
Implementation and Planning
Study and Quality Management
Hadron Collider Physics
Hadron Collider Experiments
Lepton Collider Physics
Lepton Collider Experiments
Lepton-Hadron Collider Physics
Lepton-Hadron Collider Experiment
Hadron Injectors
Hadron Collider
Lepton Injectors
Lepton Collider
Lepton-Hadron Collider
Technology R&D
Civil Engineering
Technical Infrastructures
Operation and Energy Efficiency
Integration
Computing and Data Services
Safety, RP and Environment
Project Risk Assessment
Implementation Scenarios
Cost Models
Study Administration
Communications
Conceptual Design Report
Work Breakdown Structure

## Slide 71
Physics and Experiments
Accelerators
Infrastructures and Operation
Implementation and Planning
Study and Quality Management
Hadron Collider Physics
Hadron Collider Experiments
Lepton Collider Physics
Lepton Collider Experiments
Lepton-Hadron Collider Physics
Lepton-Hadron Collider Experiment
Hadron Injectors
Hadron Collider
Lepton Injectors
Lepton Collider
Lepton-Hadron Collider
Technology R&D
Civil Engineering
Technical Infrastructures
Operation and Energy Efficiency
Integration
Computing and Data Services
Safety, RP and Environment
Project Risk Assessment
Implementation Scenarios
Cost Models
Study Administration
Communications
Conceptual Design Report
WBS – H2020 EU DS proposal

## Slide 72
PSB
PS (0.6 km)
SPS (6.9 km)
HL-LHC
FCC-ee (80-100 km,
e+e-, up to 350
or 500 GeV c.m.)
FCC-hh
(pp up to
100 TeV c.m.
& AA)
FCC-he: e± (60-250 GeV) – p(50 TeV)/A collisions
≥50 years e+e-, pp, e±p/A physics at highest energies
LHeC & SAPPHiRE (gg)
LHC (26.7 km)
LHeC as FCC-ee injector?
LHeC-based FCC-he collider?!
FCC-he as ring-ring
collider ?!
possible evolution of FCC complex

## Slide 73: is history repeating itself…?
When Lady Margaret Thatcher visited CERN in 1982, she also asked the then CERN Director-General Herwig Schopper how big the next tunnel after LEP would be.
Herwig Schopper, private communication, 2013
Margaret Thatcher,
British PM 1979-90
Herwig Schopper
CERN DG 1981-88
built LEP
John Adams
CERN DG 1960-61 & 1971-75
built PS & SPS
maybe the Prime Minister was right!?
Dr. Schopper‘s answer was there would be no bigger tunnel at CERN.
Lady Thatcher replied that she had „obtained exactly the same answer from Sir John Adams when the SPS was built“ 10 years earlier, and therefore she didn‘t believe him.

## Slide 74
HEP time scale
1980
1985
1995
2000
2005
2010
2015
2020
2025
2030
2035
1990
Physics
25 years
Today
CDR & Cost
Construc-tion
Physics
Upgr
LEP
Construction
Physics
Proto
Design
LHC
Construct
Physics
Design
HL-LHC
Construction
Proto
Design
Future Collider

## Slide 75
First FCC Week
Conference
Washington DC
23-27 March 2015
http://cern.ch/fccw2015
++...

## Slide 76
hoping to see you there!
… despite the unpromising historical precedence
First FCC Week, Washington DC
23-27 March 2015 – DRAFT SCHEDULE

## Slide 77
„Wenn mein Sohn von Frankfurt nach Mainz reist, so bringt er mehr Kenntnis heim als andere aus Amerika.“
Catharina Elisabeth Goethe

## Slide 79: spare slides

## Slide 80
 | S-KEKB | SLC | CLIC (3 TeV) | ILC (H) | FCC-ee (H)
e+ / second | 2.5 x 1012 | 6 x 1012 | 110 x 1012 | 200 x 1012 | 0.05 x 1012
e+ source – rate requirements
X 18
X 33
/ 120
L. Rinolfi
20x106
ILC e+ source has no precedent; its performance can be verified only after ILC construction (needs >150 GeV e- beam)
ILC e+ source design
5x10-5 b-1/e+
1 b-1/e+
efficiency of e+ usage:
factor 20000

## Slide 81
 | Unit | LHC Design | FCC-hh | FCC-hh
operation mode | - | Pb-Pb | Pb-Pb | p-Pb
number of bunches |  | 592 | 432 | 432
part. / bunch | [108] | 0.7 | 1.4 | 115(1.4)/1.4
β-functionat IP | [m] | 0.5 | 1.1 | 1.1
RMS beam size at IP | [um] | 15.9 | 8.8 | 8.8
initial luminosity | [1027cm-2s-1] | 1 | 3.2 | 267(3.2)
peak luminosity | [1027cm-2s-1] | 1 | 12.7 | 5477(3356)
integr. lumi. per fill | [mb-1] | <15 | 83 | 30240
total cross-section | [b] | 515 | 597 | 2
initial luminosity lifetime | [h] | <5.6 | 3.7 | 3.2 (10.6)
M. Schaumann, J. Jowett
preliminary parameters
FCC as heavy-ion collider

## Slide 82
parameter | LEP2 | FCC-ee |  |  |  |  | CepC
 |  | Z | Z (c.w.) | W | H | t | H
Ebeam [GeV] | 104 | 45 | 45 | 80 | 120 | 175 | 120
circumference [km] | 26.7 | 100 | 100 | 100 | 100 | 100 | 54
current [mA] | 3.0 | 1450 | 1431 | 152 | 30 | 6.6 | 16.6
PSR,tot [MW] | 22 | 100 | 100 | 100 | 100 | 100 | 100
no. bunches | 4 | 16700 | 29791 | 4490 | 1360 | 98 | 50
Nb [1011] | 4.2 | 1.8 | 1.0 | 0.7 | 0.46 | 1.4 | 3.7
ex [nm] | 22 | 29 | 0.14 | 3.3 | 0.94 | 2 | 6.8
ey [pm] | 250 | 60 | 1 | 1 | 2 | 2 | 20
b*x [m] | 1.2 | 0.5 | 0.5 | 0.5 | 0.5 | 1.0 | 0.8
b*y [mm] | 50 | 1 | 1 | 1 | 1 | 1 | 1.2
s*y [nm] | 3500 | 250 | 32 | 130 | 44 | 45 | 160
sz,SR [mm] | 11.5 | 1.64 | 2.7 | 1.01 | 0.81 | 1.16 | 2.3
sz,tot [mm] (w beamstr.) | 11.5 | 2.56 | 5.9 | 1.49 | 1.17 | 1.49 | 2.7
hourglass factor Fhg | 0.99 | 0.64 | 0.94 | 0.79 | 0.80 | 0.73 | 0.61
L/IP [1034 cm-2s-1] | 0.01 | 28 | 212 | 12 | 6 | 1.7 | 1.8
tbeam [min] | 300 | 287 | 39 | 72 | 30 | 23 | 40

## Slide 83
parameter | LEP2 | FCC-ee |  |  |  | 
 |  | Z | Z (c.w.) | W | H | t
Ebeam [GeV] | 104 | 45 | 45 | 80 | 120 | 175
circumference [km] | 26.7 | 100 | 100 | 100 | 100 | 100
current [mA] | 3.0 | 1450 | 1431 | 152 | 30 | 6.6
PSR,tot [MW] | 22 | 100 | 100 | 100 | 100 | 100
no. bunches | 4 | 16700 | 29791 | 4490 | 1360 | 98
Nb [1011] | 4.2 | 1.8 | 1.0 | 0.7 | 0.46 | 1.4
ex [nm] | 22 | 29 | 0.14 | 3.3 | 0.94 | 2
ey [pm] | 250 | 60 | 1 | 1 | 2 | 2
b*x [m] | 1.2 | 0.5 | 0.5 | 0.5 | 0.5 | 1.0
b*y [mm] | 50 | 1 | 1 | 1 | 1 | 1
s*y [nm] | 3500 | 250 | 32 | 84 | 44 | 45
sz,SR [mm] | 11.5 | 1.64 | 2.7 | 1.01 | 0.81 | 1.16
sz,tot [mm] (w beamstr.) | 11.5 | 2.56 | 5.9 | 1.49 | 1.17 | 1.49
hourglass factor Fhg | 0.99 | 0.64 | 0.94 | 0.79 | 0.80 | 0.73
L/IP [1034 cm-2s-1] | 0.01 | 28 | 212 | 12 | 6 | 1.7
tbeam [min] | 434 | 298 | 39 | 73 | 29 | 21
FCC-ee baseline parameters defined in EDMS No. 1346081, FCC-ACC-SPC-0003 (Rev. 2.0)
the large number of bunches at Z, W & H requires 2 rings
short lifetimes due to high luminosity → continuous injection (top-up)

## Slide 84
parameter | LEP2 | FCC-ee |  |  |  | 
 |  | Z | Z (c.w.) | W | H | t
Ebeam [GeV] | 104 | 45 | 45 | 80 | 120 | 175
beam-beam par. xy/IP | 0.06 | 0.03 | 0.175 | 0.06 | 0.093 | 0.092
current [mA] | 3.0 | 1450 | 1431 | 152 | 30 | 6.6
PSR,tot [MW] | 22 | 100 | 100 | 100 | 100 | 100
no. bunches | 4 | 16700 | 29791 | 4490 | 1360 | 98
Nb [1011] | 4.2 | 1.8 | 1.0 | 0.7 | 0.46 | 1.4
ex [nm] | 22 | 29 | 0.14 | 3.3 | 0.94 | 2
ey [pm] | 250 | 60 | 1 | 1 | 2 | 2
b*x [m] | 1.2 | 0.5 | 0.5 | 0.5 | 0.5 | 1.0
b*y [mm] | 50 | 1 | 1 | 1 | 1 | 1
s*y [nm] | 3500 | 250 | 32 | 84 | 44 | 45
sz,SR [mm] | 11.5 | 1.64 | 2.7 | 1.01 | 0.81 | 1.16
sz,tot [mm] (w beamstr.) | 11.5 | 2.56 | 5.9 | 1.49 | 1.17 | 1.49
hourglass factor Fhg | 0.99 | 0.64 | 0.94 | 0.79 | 0.80 | 0.73
L/IP [1034 cm-2s-1] | 0.01 | 28 | 212 | 12 | 6 | 1.7
tbeam [min] | 434 | 298 | 39 | 73 | 29 | 21

## Slide 85: comparison of key design parameters
Parameter | LEP2 | FCC-ee |  |  | ILC |  | 
 |  | Z | H | t | H | 500 | 1 TeV
E (GeV) | 104 | 45 | 120 | 175 | 125 | 250 | 500
<I (mA)> | 4 | 1400 | 30 | 7 | 0.000021 | .000021 | .000027
P SR/b,tot [MW] | 22 | 100 | 100 | 100 | 5.9 | 10.5 | 27.2
PAC [MW] | ~200 | ~260 | ~270 | ~300 | ~129 | ~163 | ~300
hwall→beam [%] | ~30 | 30-40 | 30-40 | 30-40 | 4.6 | 6.4 | 9.1
Nbunch/ring (pulse) | 4 | 16’700 | 1’330 | 98 | 1312 | 1312 | 2450
fcoll (kHz) | 45 | 50000 | 4000 | 294 | 6.6 | 6.6 | 9.8
b*x/y (mm) | 1500/ 50 | 500 / 1 | 500 /1 | 1000/1 | 13 | 11 | 11
ex (nm) | 30-50 | 29 | 1 | 2 | 0.04 | 0.02 | 0.01
ey (pm) | ~250 | 60 | 2 | 2 | 0.14 | 0.07 | 0.03
xy (ILC: ng) | 0.07 | 0.03 | 0.09 | 0.09 | (1.12) | (1.72) | (2.12)
nIP | 4 | 4 | 4 | 4 | 1 | 1 | 1
L0.01/IP | 0.012 | 28 | 6.0 | 1.8 | 0.65 | 1.05 | 2.2
L0.01,tot (1034 cm-2s-1) | 0.048 | 112 | 24 | 7.2 | 0.65 | 1.05 | 2.2

## Slide 86
e+e- luminosity vs energy
additional ILC upgrades
(Harrison, Ross, Walker, 2013)
FCC-ee crab waist / improved optics
(Bogomyagkov, Levichev, Piminov, Shatilov, 2014)

## Slide 87
collider parameters | FCC ERL | FCC-ee ring |  | protons
species | e- (e+?) | e± | e± | p
beam energy [GeV] | 60 | 60 | 120 | 50000
bunches / beam | - | 10600 | 1360 | 10600
bunch intensity [1011] | 0.05 | 0.94 | 0.46 | 1.0
beam current [mA] | 25.6 | 480 | 30 | 500
rms bunch length [cm] | 0.02 | 0.15 | 0.12 | 8
rms emittance [nm] | 0.17 | 1.9 (x) | 0.94 (x) | 0.04 [0.02 y]
bx,y*[mm] | 94 | 8, 4 | 17, 8.5 | 400 [200 y]
sx,y* [mm] | 4.0 | 4.0, 2.0 |  | equal
beam-b. parameter x | (D=2) | 0.13 | 0.13 | 0.022 (0.0002)
hourglass reduction | 0.92 (HD=1.35) | ~0.21 | ~0.39 | 
CM energy [TeV] | 3.5 | 3.5 | 4.9 | 
luminosity[1034cm-2s-1] | 1.0 | 6.2 | 0.7 | 
preliminary FCC-he parameters shown at ICHEP’14

## Slide 88
Upgradeable to 1 GeV – parameter sets also available
ILC parameters (TDR)

## Slide 89: Possible CLIC stages studied in the CDR
Key features:
High gradient (energy/length)
Small beams (luminosity)
Repetition rates and bunch spacing (experimental conditions)
S. Stapnes

## Slide 90: crab crossing
crossing angle reduces
luminosity, reduction factor
effective cross section
principle of
crab crossing:
effect worse for smaller b*,

## Slide 92: Future Highest-Energy Circular Colliders In preparation for the post-LHC era, the Future Circular Collider (FCC) study, launched in early 2014, is developing a 100-TeV c.m. proton-proton collider (FCC-hh), based on 16-T Nb3Sn magnets and a new 100-km tunnel infrastructure. The FCC study also includes the design of a high-luminosity e+e- collider in the same tunnel (FCC-ee, formerly TLEP), operating at c.m. energies from 91 GeV up to 350-500 GeV, as a potential intermediate step. In addition, the FCC study considers a highest-energy proton-lepton option (FCC-he). A parallel design study in China prepares for a similar, but smaller e+e-/pp collider, called CepC/SppC. FCC-hh, FCC-ee, and FCC-he offer a rich and complementary physics programme at the high-energy frontier. The key design challenges for FCC-ee include efficient high-gradient cw SRF systems, top-up injection scheme, optics design for arcs and final focus, effects of beamstrahlung, beam polarization, energy calibration, as well as power consumption. FCC-hh faces other challenges, such as high-field magnets, machine protection, and the effective handling of large synchrotron radiation power in a superconducting machine. Depending on the LHC results and on decisions taken elsewhere, several possible scenarios and alternative evolutions of the CERN complex can be conceived.

## Slide 93: To do
European magnet test 11-T dipole