## Slide 1
Future Circular Colliders
http://cern.ch/fcc
FCC
PS
SPS
LHC
Frank Zimmermann
gratefully acknowledging input from FCC coordination group, study leader Michael Benedikt, the global design study team and all international contributors
Ruprecht-Karls-Universität Heidelberg, 31 May 2016
Work supported by the European Commission under Capacities 7th Framework Programme project EuCARD-2, grant agreement 312453, and the HORIZON 2020 project EuroCirCol, grant agreement 654305

## Slide 2
Motivation for Future Circular Colliders
FCC Study Scope & Time Line
Machine Design, Physics, Detectors
Technologies
FCC Organisation & Collaboration
Outline

## Slide 3
European Strategy for Particle Physics 2013:
  “…to propose an ambitious post-LHC accelerator project….., CERN should undertake design studies for accelerator projects in a global context,…with emphasis on proton-proton and electron-positron high-energy frontier machines….coupled to a vigorous accelerator R&D programme, including high-field magnets and high-gradient accelerating structures,….”
U.S. strategy and P5 recommendation 2014:
  ”….A very high-energy proton-proton collider is the most powerful tool for direct discovery of new particles and interactions under any scenario of physics results that can be acquired in the P5 time window….”
FCC strategic motivation
ICFA statement 2014:
  ”…. ICFA supports studies of energy frontier circular colliders and encourages global coordination.….”

## Slide 4
A very large circular hadron collider seems the only approach to reach 100 TeV c.m. collision energy in coming decades
Access to new particles (direct production) in the few TeV to 30 TeV mass range, far beyond LHC reach.
Much-increased rates for phenomena in the sub-TeV mass range →increased precision w.r.t. LHC and possibly ILC
FCC motivation:
pushing the energy frontier
The name of the game of a hadron collider is energy reach
Cf. LHC: factor ~4 in radius, factor ~2 in field  O(10) in Ecms

## Slide 5
International FCC collaboration (CERN as host lab) to study:
pp-collider O(100) TeV (FCC-hh)  main emphasis, defining infrastructure requirements
80-100 km tunnel infrastructure in Geneva area
e+e- collider (FCC-ee) as potential intermediate step
p-e (FCC-he) option
HE-LHC with FCC-hh technology
~16 T  100 TeV pp in 100 km
Future Circular Collider Study
GOAL: CDR and cost review for the next ESU (2018)

## Slide 6
CepC/SppC study (CAS-IHEP) 54 km (baseline)
e+e- collisions ~2028; pp collisions ~2042
Qinhuangdao (秦皇岛）
easy access
300 km east
from Beijing
3 h by car
1 h by train
Yifang Wang
CepC, SppC
“Chinese Toscana”
100 km
50 km

## Slide 7
ex. SSC
Supercolliders Superdetectors: Proceedings of the 19th and 25th Workshops of the INFN Eloisatron Project
ex. ELOISATRON
SSC CDR 1986
H. Ulrich Wienands, The SSC Low Energy Booster: Design and Component Prototypes for the First Injector Synchrotron, IEEE Press, 1997
VLHC Design Study Group Collaboration
June 2001. 271 pp.
SLAC-R-591, SLAC-R-0591, SLAC-591,
SLAC-0591, FERMILAB-TM-2149
http://www.vlhc.org/
ex. VLHC
Tristan-II
option 2
ex. TRISTAN II
Tristan-II
option 1
F. Takasaki
Previous studies in Italy (ELOISATRON 300km), USA (SSC 87km, VLHC 233km), Japan (TRISTAN-II 94km)
many aspects of machine design and R&D non-site specific
exploit synergies with other projects & previous studies

## Slide 8
FCC-hh: 100 TeV pp collider as long-term goal  defines infrastructure needs
FCC-ee: e+e- collider, potential intermediate step
HE-LHC: based on FCC-hh technology
tunnel infrastructure in Geneva area, linked to CERN accelerator complex;
site-specific, as requested by European strategy
key technologies pushed in dedicated R&D programmes, e.g.
16 Tesla magnets for 100 TeV pp in 100 km
SRF technologies and RF power sources
FCC Scope:
Accelerator and Infrastructure

## Slide 9
physics opportunities
discovery potentials
experiment concepts for hh, ee and he
machine Detector Interface studies
concepts for worldwide data services
overall cost model ;
cost scenarios for collider options
including infrastructure and injectors ;
implementation and governance models
FCC Scope:
Physics & Experiments

## Slide 10
Constr.
Physics
LEP
Construction
Physics
Proto
Design
LHC
Construction
Physics
Design
HL-LHC
Physics
Construction
Proto
1980
1985
1990
1995
2000
2005
2010
2015
2020
2025
2030
2035
20 years
CERN Circular Colliders and FCC
Design
FCC
now is the right time to plan for the period 2035 – 2040
goal of phase 1: CDR by end 2018 for next update of European Strategy

## Slide 11
Progress on site investigations
Notes: Use the latest slides from John/Charlie.
100 km machines, possibly with both versions intersecting and non-intersecting?

## Slide 12
90 – 100 km fits geological situation well
LHC suitable as potential injector
The 100 km version, intersecting LHC, is now being studied in more detail
Progress on site investigations
Notes: Use the latest slides from John/Charlie.
100 km machines, possibly with both versions intersecting and non-intersecting?

## Slide 13
Further CE and TI optimisation
More detailed studies launched on
CE: single vs. double tunnels
CE: caverns, shafts, underground layout
technical infrastructures
safety, access
transport, integration, installation
operation aspects
Notes: Studies are now shifting more on integration aspects, safety, access, installation.
Single vs. double tunnels, optimisation of cross sesctions, etc.

## Slide 14
100 km FCC
intersecting version
current baseline is to fully re-use the existing CERN accelerator complex
injection energy 3.3 TeV from LHC
injector options:
SPS  LHC  FCC
SPS/SPSupgrade  FCC
SPS -> FCC booster  FCC
FCC-hh injector studies
SPS
FCC
Notes: See talk of Oliver on injection energy
Several options, present baseline is 3.3 GeV
Ínjection at 1.5 TeV studied as alternative, potentially compatible with SPS upgrade

## Slide 15
parameter | FCC-hh |  | HE-LHC* | (HL) LHC
collision energy cms [TeV] | 100 |  | >25 | 14
dipole field [T] | 16 |  | 16 | 8.3
circumference [km] | 100 |  | 27 | 27
# IP | 2 main & 2 |  | 2 & 2 | 2 & 2
beam current [A] | 0.5 |  | 1.27 | (1.12) 0.58
bunch intensity [1011] | 1 | 1 (0.2) | 2.5 | (2.2) 1.15
bunch spacing [ns] | 25 | 25 (5) | 25 | 25
beta* [m] | 1.1 | 0.3 | 0.25 | (0.15) 0.55
luminosity/IP [1034 cm-2s-1] | 5 | 20 - 30 | >25 | (5) 1
events/bunch crossing | 170 | <1020 (204) | >850 | (135) 27
stored energy/beam [GJ] | 8.4 |  | 1.4 | (0.7) 0.36
synchrotron rad. [W/m/beam] | 30 |  | 4.1 | (0.35) 0.18
*tentative
Hadron collider parameters

## Slide 16
phase 1: b*=1.1 m, DQtot=0.01, tta=5 h, 250 fb-1 / year
phase 2: b*=0.3 m, DQtot=0.03, tta=4 h, 1 ab-1 / year
radiation damping: t~1 h
FCC-hh luminosity phases
PRST-AB 18, 101002 (2015)
Total integrated luminosity over 25 years operation
O(20) ab-1
consistent with
physics goals

## Slide 17
Physics prospects

## Slide 18
Higgs & EWSB physics at 100 TeV
huge production rates at 100 TeV imply:
can afford reducing statistics, with tighter kinematical cuts that reduce backgrounds and systematics
explore new dynamical regimes, with novel tests of the SM and EWSB
Contino, Lee, Michelangelo, Reuter

## Slide 19
LHC results: need for higher energy
G. Giudice

## Slide 20
FCC-hh physics perspectives
G. Giudice

## Slide 21
full ring optics design
available as basis for:
beam dynamics studies
optimisation of each insertion
definition of system specifications (apertures, etc.)
improvement of baseline optics and layout
FCC-hh full-ring optics design
Regular arc cell
Interaction region
Betatron collimation
Momentum collim.
Injection with RF
Extraction/dumping
Notes: Add one slide showing optics, possibly with some smaller plots on insertions?
Detailed optimisation on optics of each insertion within overall defined boundaries.

## Slide 22
FCC-hh MDI studies
design of interaction region
consistent for machine and detector
  L*=45 m
  integrated spectrometer and compensation dipoles
optics with long triplet with large aperture
  helps distributing collision debris
  more beam stay clear
Notes: Add one slide showing optics, possibly with some smaller plots on insertions?
Detailed optimisation on optics of each insertion within overall defined boundaries.

## Slide 23
protecting triplet from debris
total power of background events 100-500 kW per experiment
car or truck engine
already limit in LHC and HL-LHC
magnet lifetime, heat load
study of 3000 fb-1 in older FCC-hh detector design
goal: survive at least 5000 fb-1
one 5-year run
shield (TAS)
magnets
dose for
3000 fb-1
30 MGy =
present limit
shielding
5mm
10mm
15mm
20mm
M. I. Besana, F. Cerutti, et al.

## Slide 24
some design challenges:
large η acceptance
radiation levels of >50 x LHC Phase II
pileup of ~1000
a B=6 T, R=6 m solenoid with shielding coil and 2 dipoles has been engineered in detail. Alternative magnet systems are being studied
detector concepts for 100 TeV pp
R&D for FCC detectors is a natural continuation of the R&D for LHC Phase II upgrade
parametrized detector performance model (DELPHES) is available and integrated in FCC software framework for physics simulations
  https://twiki.cern.ch/twiki/bin/view/FCC/FccPythiaDelphes
Notes: See with Werner about detector

## Slide 25
physics/detector simulation software
parametrized detector performance (DELPHES) is integrated in the FCC software framework and ready to use.
https://twiki.cern.ch/twiki/bin/view/FCC/FccPythiaDelphes
full simulation functional
reconstruction and fast simulation are very advanced
lots of effort on updating documentation and infrastructure
single entry point for all information: http://fccsw.web.cern.ch/fccsw/
Combined
Muon only
Tracker only
calorimeter resolution, containment studies
muon system performance studies and requirements
Notes: See wth Werner for 1 slde on this

## Slide 26
High-Energy LHC (HE-LHC)
FCC study continues effort on high-field collider in LHC tunnel
2010 EuCARD Workshop Malta;
Yellow Report CERN-2011-1
based on 16-T dipoles developed for FCC-hh
extrapolation of other parts from the present (HL-)LHC
and from FCC developments
EuCARD-AccNet-EuroLumi Workshop: The High-Energy Large Hadron Collider - HE-LHC10,
E. Todesco and F. Zimmermann (eds.), EuCARD-CON-2011-001; arXiv:1111.7188; CERN-2011-003 (2011)

## Slide 27
HE-LHC - 25 TeV c.m.
b*=25 cm or 15 cm
very preliminary

## Slide 28
HE-LHC: pile up & performance
with 160 days of physics, 70% availability, 3 h turnaround time
b*=25 cm: 920 fb-1/year
b*=15 cm: 1100 fb-1/year
very preliminary
M. Benedikt, S. Fartoukh, F. Zimmermann
pile up of 1000 or shorter (e.g. 5 ns) bunch spacing – what is easier?
25 ns bunch spacing

## Slide 29
FCC–ee: physics requirements
physics programs / energies:
  Z (45.5 GeV) Z pole, ‘TeraZ’ and high precision MZ & GZ
  W (80 GeV) W pair production threshold, high precision MW
  H (120 GeV) ZH production (maximum rate of H’s)
  t (175 GeV): threshold, H studies
beam energy range from 35 GeV to 200 GeV
highest possible luminosities at all working points
possibly H (63 GeV) direct s-channel production with monochromatization
some polarization up to ≥80 GeV for precise beam energy calibration (<100 keV)

## Slide 30
identical FCC-ee baseline optics for all energies
FCC-ee: 2 separate rings LEP: single beam pipe
parameter | FCC-ee (400 MHz) |  |  |  |  | LEP2
Physics working point | Z |  | WW | ZH | ttbar | 
energy/beam [GeV] | 45.6 |  | 80 | 120 | 175 | 105
bunches/beam | 30180 | 91500 | 5260 | 780 | 81 | 4
bunch spacing [ns] | 7.5 | 2.5 | 50 | 400 | 4000 | 22000
bunch population [1011] | 1.0 | 0.33 | 0.6 | 0.8 | 1.7 | 4.2
beam current [mA] | 1450 | 1450 | 152 | 30 | 6.6 | 3
luminosity/IP x 1034cm-2s-1 | 210 | 90 | 19 | 5.1 | 1.3 | 0.0012
energy loss/turn [GeV] | 0.03 | 0.03 | 0.33 | 1.67 | 7.55 | 3.34
synchrotron power [MW] | 100 |  |  |  |  | 22
RF voltage [GV] | 0.4 | 0.2 | 0.8 | 3.0 | 10 | 3.5
lepton collider parameters

## Slide 31
FCC-ee
Barry Barish
13 January 2011
DAFNE
VEPP2000
combining successful ingredients of recent colliders → extremely high luminosity at high energies
LEP:
high energy
SR effects
B-factories:
KEKB & PEP-II:
high beam
currents
top-up injection
DAFNE: crab waist
Super B-factories
S-KEKB: low by*
KEKB: e+ source
HERA, LEP, RHIC:
spin
gymnastics
FCC-ee exploits lessons & recipes from past e+e- and pp colliders
TRISTAN

## Slide 32
new baseline crab waist with 2 IPs
by*=2 mm, bx*=1 m
CEPC
further increase with squeeze to by*=1 mm, bx*=0.5 m
Z
WW
HZ
aQED
?
solid baseline with functioning optics, space for improvement, esp. at Z and W
FCC-ee luminosity per IP

## Slide 33
2 main IPs in A, G for both machines
asymmetric IR optic/geometry for ee to limit synchrotron radiation to detector
common layouts for hh & ee
11.9 m
30 mrad
9.4 m
FCC-hh/
ee Booster
Common
RF (tt)
Common
RF (tt)
IP
IP
0.6 m
Max. separation of 3(4) rings is about 12 m:
wider tunnel or two tunnels are necessary around the IPs, for ±1.2 km.
Lepton beams must cross over through the common RF to enter the IP from inside.
Only a half of each ring is filled with bunches.
FCC-ee 1, FCC-ee 2,
FCC-ee booster (FCC-hh footprint)
FCC-hh
layout
Notes: Check with Katsunobu to have latest layout.
Check with detector people if 9 m offset is acceptable for ee detector

## Slide 34
FCC-ee optics design
IP
Beam
Local chromaticity correction
+ crab waist sextupoles
Local chromaticity correction
+ crab waist sextupoles
optics design for all working points achieving baseline performance
interaction region: asymmetric optics design
synchrotron radiation from upstream dipoles <100 keV up to 450 m from IP
dynamic aperture & momentum acceptance requirements fulfilled at all WPs
Notes: New slide from Katsunobu on converged optics, final focus and ring optics
Sufficient dynamic aperture and momentum
Injection details missing

## Slide 35
FCC-ee full-ring optics design
dynamic aperture and momentum acceptance requirements fulfilled
45.6 GeV,
β*x,y = (0.5 m, 1 mm)
175 GeV,
β*x,y = (1 m, 2 mm)
K. Oide
Notes: New slide from Katsunobu on converged optics, final focus and ring optics
Sufficient dynamic aperture and momentum
Injection details missing

## Slide 36
beam commissioning started this year
top up injection at high current
by* =300 mm (FCC-ee: 1 mm)
lifetime 5 min (FCC-ee: ≥20 min)
ey/ex =0.25% (similar to FCC-ee)
off momentum acceptance (±1.5%, similar to FCC-ee)
e+ production rate (2.5x1012/s, FCC-ee: <1.5x1012/s (Z cr.waist)
SuperKEKB goes beyond FCC-ee, testing all concept
SuperKEKB: FCC-ee demonstrator
Ie+=3.6 A, Ie-=2.6 A
PSR ~ 13 MW
C = 3 km

## Slide 38
FCC-ee MDI optimisation
MDI work focused on optimization of
l*, IR quadrupole design
compensation & shielding solenoid
SR masking and chamber layout
CERN model of
CCT IR quadrupole
BINP prototype IR quadr.
2 cm aperture, 100 T/m
Notes: New slide on MDI optimisation, L*, solenoid compensation, lumi monitoring, etc.
Slide from Mike Sullivan talk, synchrotron radiation IR, masking?
Possibly one slide on magnet design of Attilio?

## Slide 39
FCC-hh
1
1
5
the combination of FCC-ee and FCC-hh is «invincible»
Higgs coupling summary
M. Klute
statistical
errors after
10 years of
operation

## Slide 40
synchrotron radiation/beam screen
Photon distribution
first FCC-hh beam screen prototype
testing 2017 at ANKA facility in Germany
handling of high synchrotron radiation load of protons @ 50 TeV:
~30 W/m/beam (@16 T) (LHC <0.2W/m)
5 MW total in arcs
new beam screen with ante-chamber
absorption of synchrotron radiation at 50 K to reduce cryogenic power
avoids photo-electrons, helps vacuum

## Slide 41
contributions: beam screen (BS) & cold bore (BS heat radiation)
Cryo power for cooling of SR heat
Overall optimisation of cryo-power, vacuum and impedance
Termperature ranges: <20, 40K-60K, 100K-120K
100MW
200MW
300MW
multi-bunch instability growth time: 25 turns 9 turns (DQ=0.5)
Ph. Lebrun
L. Tavian
V. Baglin

## Slide 42
Main Milestones of the FCC Magnet Program 2016 - 2019 |  |  |  |  |  |  |  |  |  |  |  |  | 
Milestone | Description | 15 | 2016 |  | 2017 |  | 2018 |  | 2019 |  | 2020 |  | 21
M0 | High Jc wire development with industry |  |  |  |  |  |  |  |  |  |  |  | 
M1 | Supporting wound conductor test program |  |  |  |  |  |  |  |  |  |  |  | 
M2 | Design & manufacture 16T ERMC with existing wire |  |  |  |  |  |  |  |  |  |  |  | 
M3 | Design & manufacture 16 T RMM with existing wire |  |  |  |  |  |  |  |  |  |  |  | 
M4 | Design & manufacture 16T demonstrator magnet |  |  |  |  |  |  |  |  |  |  |  | 
M5 | Procurement of enhanced high Jc wire |  |  |  |  |  |  |  |  |  |  |  | 
M6 | EuroCirCol design 16T accelerator quality model |  |  |  |  |  |  |  |  |  |  |  | 
 | Manufacture and test of the 16 T EuroCirCol model |  |  |  |  |  |  |  |  |  |  |  | 
ERMC (16 T mid-plane field) RMM (16 T in 50 mm cavity) Demonstrator (16 T, 50 mm gap) mid 2017 end 2017 end 2018
CERN & EuroCirCol 16T programs
Magnets with bore
Field records
LBNL HD1
CERN RMC
16 T “dipole” levels reached with small racetrack coils
LBNL 2004, CERN 2015

## Slide 43
superconductor performance
Chart: B in T
10 % margin FCC | 0 | 0.952
10% margin HL-LHC | 0 | 0.6831
16 T | 0 | 1.5
3150 mm2
~1.7 times less SC
~10% margin
HL-LHC
5400 mm2
16 T
Critical surface FCC
HL-LHC
Nb3Sn T = 4.5 K
LHC at 1.9 K
Nb-Ti
Not possible
Different technology
~10% margin
FCC ultimate

## Slide 44
Nb3Sn conductor program
Nb3Sn conductor is one of the major cost and performance factors for FCC-hh and must be given highest attention
Goals: Jc increase (16 T, 4.2 K) > 1500 A/mm2, significant cost reduction
Actions ongoing and planned (in addition to activities at CERN):
  Purchase of wires in Europe, US
  Industrial R&D in Europe
  Collaboration agreements with KEK, Russia, Korea (in preparation), to stipulate conductor development with regional industry
  Collaborations with several European Universities and Research Centres
U.S. Magnet Development Program with conductor R&D program and focused on 16 T cos theta dipole model magnet.
Notes: New slide from Davide.
Showing that conductor development is launched at international level, Russia, Japan, (Korea and Europe in preparation)
Underline importance of that development as main cost driver for the hadron collider machine.

## Slide 45
RF system requirements
 | Vtotal GV | nbunches | Ibeam mA | DE/turn GeV
hh | 0.032 |  | 500 | 
Z | 0.4/0.2 | 30000/90000 | 1450 | 0.034
W | 0.8 | 5162 | 152 | 0.33
H | 5.5 | 770 | 30 | 1.67
t | 10 | 78 | 6.6 | 7.55
“Ampere-class” machines
“high gradient” machines
x6
≈ 16 x 1 cell 400MHz,
x12
Naive scale up from an hh system
very large range of operation parameters
voltage and beam current ranges span more than factor > 102
no well-adapted single RF system solution satisfying requirements
Notes: New slide from Olivier
Common design for hadron and lepton low energy-high currecnt system
Synergies HL-LHC, HE LHC, FCC-hh, FCC-ee Z pole

## Slide 46
RF system R&D lines
hh
≈ 16 cells per beam
≈ 100 per beam
(+ 100 for booster ring)
Z
W
≈ 210 per beam
(+ 210 for booster ring)
W
≈ 800 per beam
(+ 800 for booster)
≈ common 2600 cells for both beams
(+ 2600 for booster)
H
t
≈ 200 per beam
(+ 200 for booster)
400 MHz single-cell cavities preferred for hh and ee-Z (few MeV/m)
Baseline Nb/Cu @4.5 K, development with synergies to HL-LHC, HE-LHC
R&D: power coupling 1 MW/cell, HOM power handling (damper, cryomodule)
400 or 800 MHz multi-cell cavities preferred for ee-H, ee-tt and ee-W
Baseline options 400 MHz Nb/Cu @4.5 K, ◄▬► 800 MHz bulk Nb system @2K
R&D: High Q0 cavities, coating, long-term: Nb3Sn like components
Notes: New slide from Olivier
Common design for hadron and lepton low energy-high currecnt system
Synergies HL-LHC, HE LHC, FCC-hh, FCC-ee Z pole

## Slide 47
A consortium of partners based on a Memorandum Of Understanding (MoU)
Working together on a best effort basis
Pursuing the same common goal
Self governed
Incremental & open to academia and industry
FCC Collaboration

## Slide 48
75 institutes
26 countries + EC
Status: April, 2016
FCC International Collaboration

## Slide 49
ALBA/CELLS, Spain
Ankara U., Turkey
U Belgrade, Serbia
U Bern, Switzerland
BINP, Russia
CASE (SUNY/BNL), USA
CBPF, Brazil
CEA Grenoble, France
CEA Saclay, France
CIEMAT, Spain
Cinvestav, Mexico
CNRS, France
CNR-SPIN, Italy
Cockcroft Institute, UK
U Colima, Mexico
UCPH Copenhagen, Denmark
CSIC/IFIC, Spain
TU Darmstadt, Germany
TU Delft, Netherlands
DESY, Germany
DOE, Washington, USA
ESS, Lund, Sweden
TU Dresden, Germany
Duke U, USA
EPFL, Switzerland
UT Enschede, Netherlands
U Geneva, Switzerland
Göthe U Frankfurt, Germany
GSI, Germany
GWNU, Korea
U. Guanajuato, Mexico
Hellenic Open U, Greece
HEPHY, Austria
U Houston, USA
IIT Kanpur, India
IFJ PAN Krakow, Poland
INFN, Italy
INP Minsk, Belarus
U Iowa, USA
IPM, Iran
UC Irvine, USA
Istanbul Aydin U., Turkey
JAI, UK
JINR Dubna, Russia
Jefferson LAB, USA
FZ Jülich, Germany
KAIST, Korea
KEK, Japan
KIAS, Korea King’s College London, UK
KIT Karlsruhe, Germany
KU, Seoul, Korea
Korea U Sejong, Korea
U. Liverpool, UK U. Lund, Sweden
MAX IV, Lund, Sweden
MEPhI, Russia UNIMI, Milan, Italy
MIT, USA
Northern Illinois U, USA
NC PHEP Minsk, Belarus
U Oxford, UK
PSI, Switzerland
U Rostock, Germany
RTU, Riga, Latvia
UC Santa Barbara, USA Sapienza/Roma, Italy
U Siegen, Germany
U Silesia, Poland
TU Tampere, Finland
TOBB, Turkey
U Twente, Netherlands
TU Vienna, Austria Wigner RCP, Budapest, Hungary
Wroclaw UT, Poland
FCC Collaboration Status
75 collaboration members & CERN as host institute, April 2016

## Slide 50
Supports and makes essential contributions to the FCC-hh work packages:
Arc & IR optics design, 16 T dipole design, cryogenic beam vacuum system
Recognition of FCC Study by European Commission.
European Union contributes with funding to FCC-hh study
EuroCirCol EU Horizon 2020 Grant

## Slide 51: EuroCirCol Consortium + Associates
Japan
KEK
Finland
TUT
France
CEA, CNRS
Italy
INFN
Germany
KIT, TUD
Switzerland
EPFL, UNIGE
Netherlands
UT
Spain
ALBA, CIEMAT
CERN
United Kingdom
STFC, UNILIV, UOXF
CERN | IEIO
TUT | Finland
CEA | France
CNRS | France
KIT | Germany
TUD | Germany
INFN | Italy
UT | Netherlands
ALBA | Spain
CIEMAT | Spain
STFC | United Kingdom
UNILIV | United Kingdom
UOXF | United Kingdom
KEK | Japan
EPFL | Switzerland
UNIGE | Switzerland
NHFML-FSU | USA
BNL | USA
FNAL | USA
LBNL | USA
Consortium Beneficiaries, signing the Grant Agreement

## Slide 52
First FCC Week
Conference
Washington DC
23-27 March 2015
http://cern.ch/fccw2015
“head shots” from Bob Palmer (BNL)

## Slide 53
First FCC Week
Conference
Washington DC
23-27 March 2015
http://cern.ch/fccw2015
468
Participants
24
Countries
168 Institutes
http://cern.ch/fccw2016

## Slide 54
There is a strong, rising interest in Future Circular Colliders and a community is forming to study these machines
International collaboration is needed to advance with this study on all of its challenging subjects
German expertise and participation in accelerators, experiments & physics are essential and most welcome!
Consolidated parameter sets for both machines FCC-hh and FCC-ee have been established. Work on all areas, accelerator physics, technologies, infrastructures, detectors and physics is advancing well.
Next milestone is a study review at FCC Week 2017, to define contents of the Conceptual Design Report.
Conclusions

## Slide 55: FCC Week 2017 29 May – 2 June 2017 Berlin, Germany